CHAPTER 56:  SEWERS

Section

General Provisions

56.01	Definitions

56.02	Connection requirements

56.03	Rates and charges

56.04	Tampering prohibited

Use Regulations

56.15	Tests and analyses

56.16	Character and concentration of wastes

56.17	Measurement of flow volume

56.18	Storm water surface drainage; process and cooling waters

56.19	Prohibited discharge standards; special agreements

56.20	National categorical pretreatment standards

56.21	Local limits

56.22	City's right of revision

56.23	Dilution

Industrial Wastes

56.35	Industrial wastewater discharge permits and general permits

56.36	Permit issuance

56.37	Characteristics of waters or wastes; flow

56.38	Preliminary treatment or handling

56.39	Control of prohibited wastes

56.40	Accidental discharge; treatment bypasses

56.41	Noncompliance; reporting

56.42	Reporting requirements

56.43	Records retention

56.44	Confidential information

56.45	Maximum restrictions

56.46	Discharges; disrupted service

56.47	Septage wastes

56.48	Grease traps

51

2016 S-3

52	Bennettsville - Public Works

Administration and Enforcement

56.60	Permit conditions

56.61	Pretreatment program surveillance

56.62	Inspections; authority

56.63	Notification of violations; nuisances

56.64	Compliance; schedules and orders

56.65	Show cause hearings

56.66	Cease and desist orders

56.67	Emergency suspensions

56.68	Termination of discharge

56.69	Judicial remedies; injunctive relief

56.70	Publication and severance

56.99	Penalty

GENERAL PROVISIONS

§ 56.01  DEFINITIONS.

(A)	For the purpose of this chapter, the following definitions shall apply unless the context clearly indicates or requires a different meaning.

(B)	Terms not otherwise defined in this section shall be as adopted in the latest edition of Standard Methods for the Examination of Water and Wastewater, published by the American Public Health Association, the American Water Works Association and the Water Pollution Control Federation and as in the Wastewater Treatment Plant Design Manual of Practice published by the Water Pollution Control Federation.

APPROVAL AUTHORITY. The South Carolina Department of Health and Environmental Control (SCDHEC).

AUTHORIZED or DULY AUTHORIZED REPRESENTATIVE OF THE USER.

(1)	If the user is a corporation:

(a)	The president, secretary, treasurer, or a vice-president of the corporation in charge of a principal business function, or any other person who performs similar policy or decision-making functions for the corporation; or

2016 S-3

Sewers	53

(b)	The manager of one or more manufacturing, production, or operating facilities, provided the manager is authorized to make management decisions that govern the operation of the regulated facility including having the explicit or implicit duty of making major capital investment recommendations, and initiate and direct other comprehensive measures to assure long-term environmental compliance with environmental laws and regulations; can ensure that the necessary systems are established or actions taken to gather complete and accurate information for individual wastewater discharge permit or general permit requirements; and where authority to sign documents has been assigned or delegated to the manager in accordance with corporate procedures.

(2)	If the user is a partnership or sole proprietorship: a general partner or proprietor, respectively.

(3)	If the user is a federal, state, or local governmental facility: a director or highest official appointed or designated to oversee the operation and performance of the activities of the government facility, or their designee.

(4) 	The individuals described in divisions (1) through (3), above, may designate a duly authorized representative if the authorization is in writing, the authorization specifies the individual or position responsible for the overall operation of the facility from which the discharge originates or having overall responsibility for environmental matters for the company, and the written authorization is submitted to the city.

BIOCHEMICAL OXYGEN DEMAND or BOD. The quantity of oxygen utilized in the biochemical oxidation of organic matter under standard laboratory procedures in five days at 20°C, expressed in terms of weight and concentration (milligrams per liter or ppm).

BEST MANAGEMENT PRACTICES or BMPs. Schedules of activities, prohibitions of practices, maintenance procedures, and other management practices to implement the prohibitions listed in § 56.19(A) and (B) [SC R.61-9.403.5(a)(1) and (b)]. BMPs include treatment requirements, operating procedures, and practices to control plant site runoff, spillage or leaks, sludge or waste disposal, or drainage from raw materials storage.

CATEGORICAL INDUSTRIAL USER. An industrial user subject to a categorical pretreatment standard or categorical standard.

CATEGORICAL PRETREATMENT STANDARD. Any regulation containing pollutant discharge limits promulgated by EPA in accordance with sections 307(b) and (c) of the Clean Water Act (33 U.S.C. section 1317) that apply to a specific category of users and that appear in 40 CFR Chapter I, Subchapter N, Parts 405-471.

CITY. The City of Bennettsville, the City Administrator, his designee or other designated representative of City Council, who is charged with certain duties and responsibilities by this chapter.

2016 S-3

54	Bennettsville - Public Works

CLEAN WATER ACT or ACT. The federal Water Pollution Control Act, being 33 USC 1251 et seq., Amendments of 1972, Public Law 92-500, or as they may be amended.

COLOR.  The "true color" due to substances in solution which cause any variation in the hue of the receiving stream and which is expressed, in parts per million.

COMBINED SEWER. A sewer receiving both surface run-off and sewage.

CONTROL AUTHORITY. The City of Bennettsville.

DAILY MAXIMUM. The arithmetic average of all effluent samples for a pollutant collected during a calendar day.

DAILY MAXIMUM LIMIT. The maximum allowable discharge limit of a pollutant during a calendar day. Where DAILY MAXIMUM LIMITS are expressed in units of mass, the daily discharge is the total mass discharged over the course of the day. Where DAILY MAXIMUM LIMITS are expressed in terms of a concentration, the daily discharge is the arithmetic average measurement of the pollutant concentration derived from all measurements taken that day.

DOMESTIC WASTE. Liquid wastes from non-commercial preparation, cooking and handling of food, or containing human excrement and similar matter from the sanitary conveniences of dwellings, commercial buildings, industrial facilities and institutions.

EPA. The United States Environmental Protection Agency.

EXISTING SOURCE. Any source of discharge that is not a NEW SOURCE.

GARBAGE. Solid wastes from the domestic and commercial preparation, cooking and dispensing of food and from the handling, storage and sale of produce.

GARBAGE, PROPERLY SHREDDED. The wastes from the preparation, cooking and dispensing of food which has been shredded to a degree that all particles will be carried freely under the flow conditions normally prevailing in public sewers. No particle shall be greater than one-half inch in any dimension.

GRAB SAMPLE. A sample that is taken from a wastestream without regard to the flow in the wastestream and over a period of time not to exceed 15 minutes.

HEARING AUTHORITY. The City Administrator, City Attorney, Director of Utilities and the Wastewater Treatment Superintendent or duly appointed deputies, agents or representatives thereof.

2016 S-3

Sewers	55

INDIRECT DISCHARGE. The introduction of pollutants into the POTW from any nondomestic source.

INSTANTANEOUS LIMIT. The maximum concentration of a pollutant allowed to be discharged at any time, determined from the analysis of any discrete or composited sample collected, independent of the industrial flow rate and the duration of the sampling event.

INTERFERENCE. The inhibition or disruption of the city's wastewater treatment processes or operations which contributes to a violation of any requirement of the city's NPDES permit or any applicable state or federal regulations or which results in a decrease of removal efficiency. The term includes the prevention of the use or disposal of sewage sludge and other wastewater treatment by-products.

LOCAL LIMIT. Specific discharge limits developed and enforced by the city upon industrial or commercial facilities to implement the general and specific discharge prohibitions listed in 40 CFR 403.5(a)(1) and (b).

MAY. The act is permissive.

MEDICAL WASTE. Isolation wastes, infectious agents, human blood and blood products, pathological wastes, sharps, body parts, contaminated bedding, surgical wastes, potentially contaminated laboratory wastes, and dialysis wastes.

MONTHLY AVERAGE. The sum of all daily discharges measured during a calendar month divided by the number of daily discharges measured during that month.

MONTHLY AVERAGE LIMIT. The highest allowable average of daily discharges over a calendar month, calculated as the sum of all daily discharges measured during a calendar month divided by the number of daily discharges measured during that month.

NEW SOURCE.

(1)	Any building, structure, facility, or installation from which there is (or may be) a discharge of pollutants, the construction of which commenced after the publication of proposed pretreatment standards under Section 307(c) of the Act that will be applicable to such source if such standards are thereafter promulgated in accordance with that section, provided that:

(a)	The building, structure, facility, or installation is constructed at a site at which no other source is located; or

(b)	The building, structure, facility, or installation totally replaces the process or production equipment that causes the discharge of pollutants at an existing source; or

2016 S-3

56	Bennettsville - Public Works

(c)	The production or wastewater generating processes of the building, structure, facility, or installation are substantially independent of an existing source at the same site. In determining whether these are substantially independent, factors such as the extent to which the new facility is integrated with the existing plant, and the extent to which the new facility is engaged in the same general type of activity as the existing source, should be considered.

(2)	Construction on a site at which an existing source is located results in a modification rather than a new source if the construction does not create a new building, structure, facility, or installation meeting the criteria of division (1)(b) or (c) above but otherwise alters, replaces, or adds to existing process or production equipment.

(3)	Construction of a new source as defined under this division has commenced if the owner or operator has:

(a)	Begun, or caused to begin, as part of a continuous onsite construction program:

1.	Any placement, assembly, or installation of facilities or equipment; or

2.	Significant site preparation work including clearing, excavation, or removal of existing buildings, structures, or facilities which is necessary for the placement, assembly, or installation of new source facilities or equipment; or

(b)	Entered into a binding contractual obligation for the purchase of facilities or equipment which are intended to be used in its operation within a reasonable time.  Options to purchase or contracts which can be terminated or modified without substantial loss, and contracts for feasibility, engineering, and design studies do not constitute a contractual obligation under this division.

NH3 or NITROGEN AS AMMONIA. The initial product in the decomposition of nitrogenous organic matter as measured by using standard laboratory methods, as set out in this chapter, expressed in mg/l or ppm.

NONCONTACT COOLING WATER. Water used for cooling that does not come into direct contact with any raw material, intermediate product, waste product, or finished product.

NONDOMESTIC WASTES. The liquid wastes from processes employed in institutional, commercial and industrial processes and operations, as distinct from sanitary or domestic sewage.

NPDES PERMIT. The national pollution discharge elimination system permit issued to the city pursuant to Section 402 of the Clean Water Act, being 33 USC 1342.

2016 S-3

Sewers	57

PASS THROUGH. A discharge which exits the POTW into waters of the United States in quantities or concentrations which, alone or in conjunction with a discharge or discharges from other sources, is a cause of a violation of any requirement of the city's NPDES permit, including an increase in the magnitude or duration of a violation.

pH. The logarithm (base 10) of the reciprocal of the weight of hydrogen ions in grams per liter of solution and indicating the acidity or alkalinity of a substance. A pH value of 7.0 is considered neutral, below 7.0 is acid; above 7.0 is alkaline.

PPM. Parts per million by weight.

PERSON. Any individual, partnership, copartnership, firm, company, corporation, association, joint stock company, trust, estate, governmental entity, or any other legal entity; or their legal representatives, agents, or assigns. This definition includes all federal, state, and local governmental entities.

POLLUTANT. Dredged spoil, solid waste, incinerator residue, filter backwash, sewage, garbage, sewage sludge, munitions, medical wastes, chemical wastes, biological materials, radioactive materials, heat, wrecked or discarded equipment, rock, sand, cellar dirt, municipal, agricultural and industrial wastes, and certain characteristics of wastewater (e.g., pH, temperature, TSS, turbidity, color, BOD, COD, toxicity, or odor).

PRETREATMENT. The reduction of the amount of pollutants, the elimination of pollutants, or the alteration of the nature of pollutant properties in wastewater prior to, or in lieu of, introducing such pollutants into the POTW. This reduction or alteration can be obtained by physical, chemical, or biological processes; by process changes; or by other means, except by diluting the concentration of the pollutants unless allowed by an applicable pretreatment standard.

PRETREATMENT REQUIREMENTS. Any substantive or procedural requirement related to pretreatment imposed on a user, other than a pretreatment standard.

PRETREATMENT STANDARDS or STANDARDS. Pretreatment standards shall mean prohibited discharge standards, categorical pretreatment standards, and local limits.

PROHIBITED DISCHARGE STANDARDS or PROHIBITED DISCHARGES. Absolute prohibitions against the discharge of certain substances; these prohibitions appear in § 56.19.

PUBLICLY OWNED TREATMENT WORKS or POTW. A treatment works, as defined by section 212 of the Act (33 U.S.C. section 1292), which is owned by the city. This definition includes any devices or systems used in the collection, storage, treatment, recycling, and reclamation of sewage or industrial wastes of a liquid nature and any conveyances, which convey wastewater to a treatment plant.

2016 S-3

58	Bennettsville - Public Works

RECEIVING STREAM. A body of water, stream or watercourse receiving or formed by the discharge from the wastewater treatment plant.

SANITARY SEWER. A sewer intended to receive domestic sewage and industrial waste, except that of type expressly prohibited by this division, and to which storm, surface and ground waters are not intentionally admitted.

SEPTAGE WASTE. Any sewage from holding tanks such as vessels, chemical toilets, campers, trailers, privies, cesspools and septic tanks.

SEWER. A pipe or conduit for carrying sewage.

SEWER SYSTEM. Any arrangement, devices, facilities, structures, equipment or works owned by the city for the purpose of transmitting domestic and nondomestic wastewater.

SHALL. The act is mandatory.

SIGNIFICANT INDUSTRIAL USER. Except as provided in divisions (3) and (4) below, a SIGNIFICANT INDUSTRIAL USER is:

(1)	An industrial user subject to categorical pretreatment standards; or

(2)	An industrial user that:

(a)	Discharges an average of 25,000 gpd or more of process wastewater to the POTW (excluding sanitary, noncontact cooling and boiler blowdown wastewater);

(b)	Contributes a process wastestream which makes up 5% or more of the average dry weather hydraulic or organic capacity of the POTW treatment plant; or

(c)	Is designated as such by the city on the basis that it has a reasonable potential for adversely affecting the POTW's operation or for violating any pretreatment standard or requirement.

(3)	The city, at its discretion may determine that an industrial user subject to categorical pretreatment standards is a non-significant categorical industrial user rather than a significant industrial user on a finding that the industrial user never discharges more than 100 gallons per day (gpd) of total categorical wastewater (excluding sanitary, non-contact cooling and boiler blowdown wastewater, unless specifically included in the pretreatment standard) and the following conditions are met:

(a)	The industrial user, prior to city's finding, has consistently complied with all applicable categorical pretreatment standards and requirements;

2016 S-3

Sewers	59

(b)	The industrial user annually submits the certification statement required in § 56.42(I)(2) [see SC R.61-9.403.12(q)], together with any additional information necessary to support the certification statement; and

(c)	The industrial user never discharges any untreated concentrated wastewater.

(4)	Upon a finding that a user meeting the criteria in division (2) above has no reasonable potential for adversely affecting the POTW's operation or for violating any pretreatment standard or requirement, the city may at any time, on its own initiative or in response to a petition received from an industrial user, and in accordance with procedures in SC R.61-9.403.8(f)(6), determine that such user should not be considered a significant industrial user.

SLUG LOAD or SLUG DISCHARGE. Any discharge at a flow rate or concentration, which could cause a violation of the prohibited discharge standards in § 56.19. A SLUG DISCHARGE is any discharge of a non-routine, episodic nature, including but not limited to an accidental spill or a non-customary batch discharge, which has a reasonable potential to cause interference or pass through, or in any other way violate the POTW's regulations, local limits or permit conditions.

STORM SEWER or STORM DRAIN. A sewer which carries storm and surface waters and drainage, but excludes sewage and polluted industrial wastes.

STORM WATER. Any flow occurring during or following any form of natural precipitation, and resulting from such precipitation, including snowmelt.

TOTAL SOLIDS. The sum of suspended matter, settleable matter and dissolved matter, both volatile and nonvolatile and as further defined in Standard Methods.

TOTAL SUSPENDED SOLIDS, SUSPENDED SOLIDS or TSS. The total suspended matter that floats on the surface of, or is suspended in, water, wastewater, or other liquid, and that is removable by laboratory filtering.

USER or INDUSTRIAL USER. A source of indirect discharge.

WASTEWATER. A combination of liquid and water-carried industrial and domestic wastes from dwellings, residences, commercial, buildings, institutions and industrial establishments, whether treated or untreated, together with any ground, surface and storm water that may be present which is discharged into or permitted to enter the city's wastewater treatment systems.

WASTEWATER TREATMENT PLANT or TREATMENT PLANT. Any arrangement, devices, facilities, structures, equipment or works owned by the city for the purpose of disposal, storage, treatment, recycling and reclamation of industrial and domestic wastes, including the wastewater treatment site or land that is used for the ultimate disposal of residues from the treatment.

2016 S-3

60	Bennettsville - Public Works

WASTEWATER TREATMENT SYSTEM. The entire sewer system and the entire wastewater treatment plant(s).

(Ord. 16-04-001, passed 4-19-16)

§ 56.02  CONNECTION REQUIREMENTS.

(A)	Use of public sewers.

(1)	Owners of all newly constructed houses, buildings or properties used for human occupancy, employment, recreation or other purposes, situated within the authority's boundaries and abutting on any street, alley or right-of-way in which there is a public sanitary sewer of the authority or a subdistrict, shall install at their expense suitable service lines to connect any sanitary facilities, directly with the proper public sewer in accordance with the provisions of this regulation within 90 days after the date of official notice to do so, provided the public sewer is within 300 feet of the property line and access is available. Any sewer connection to a sewer line owned by the authority shall be made at an existing manhole or a manhole constructed for that connection at the owner's expense and in accordance with the authority's regulation and specifications.

(2)	Connection of sewer service to adjacent unincorporated areas and or areas outside the city limits is outlined in this code.

(B)	General prohibitions.

(1)	The authority will prohibit privies, cesspools and septic tanks in sewer service areas when owners of houses, buildings or properties used for human occupancy, employment recreation or other purposes is situated within the authority's boundaries and abutting on any street, alley or right-of-way in which there is a public sanitary sewer of the authority.

(2)	The discharge of septic tank effluent or cesspool overflow to any drain, ditch, stream or well penetrating water bearing formation is strictly prohibited.

(3)	The discharge of sanitary wastewater, regardless of source, into the storm sewer system is strictly prohibited, without exception.

(C)	Connection of building sewer to public sewer.

(1)	Whenever possible, the building sewer shall be brought to the building at an elevation below the basement floor. In all buildings in which any building drain is too low to permit gravity flow to the public sewer, sanitary sewage carried by such building drain shall be lifted by a means approved by the authority and discharged to the building sewer.

2016 S-3

Sewers	61

(2)	The connection of the building sewer into the public sewer shall conform to the requirements of any applicable building and plumbing codes and other applicable rules and regulations of the authority. All connections shall be made gastight and watertight. Any sewer connection to a sewer owned by the authority shall be made at an existing manhole or one built for that connection at the expense of the user. Any deviation from the prescribed procedures and materials must be approved by the authority before installation.

(D)	Sewer material. All sewers, including house sewers, to be connected with or to discharge into the wastewater treatment system of the authority shall be constructed of one of the following:

(1)	Vitrified clay pipe complying with ASTM C200 and with compression type, flexible joint conforming to ASTM C425;

(2)	Cast iron pipe with a mechanical or push-on joint as described in ANSI A21.11;

(3)	ABS (acrylonitrile-butadiene-styrene) pipe and fittings conforming to ASTM D2661;

(4)	PVC (polyvinyl chloride) pipe and fittings conforming to minimum requirements of ASTM D3034, heavy wall, joint quality to conform with ASTM C425; or

(5)	Other materials specifically approved in writing by the city.

(Ord. 16-04-001, passed 4-19-16)

§ 56.03  RATES AND CHARGES.

(A)	User charge provision; surcharges. All sewer users shall participate in the user charge provision as applicable when the concentrations of BOD, TSS or NH3 in the nondomestic wastewater discharged to the city's sanitary shall be imposed upon the permitted industrial user's wastewater flow when the excess is calculated using the industrial plant water flow as specified in § 56.17 and the difference between the actual BOD, TSS or NH3 concentration and the permissible limits of 250 ppm BOD, 240 ppm TSS, or 25 ppm NH3. The surcharge shall reflect the projected cost of creating the excess pounds of nondomcsuc wastewater including necessary costs of adrninistration of the wastewater treatment works, pretreatment and sampling programs and this division.

(B)	Amount.

(1)	A surcharge of $60, per 1,000 of BOD, shall be made to cover the fixed charges and amortization costs of additional plant capacity as herein before described.

(2)	A surcharge of $90, per 1,000 of TSS, shall be made to cover the fixed charges and amortization costs of additional plant capacity as herein before described.

2016 S-3

62	Bennettsville - Public Works

(3)	A surcharge of $30, per 1,000 of NH3, shall be made to cover the fixed charges and amortization costs of additional plant capacity as herein before described.

(4)	All sewer users located outside the city limits shall pay a capital recoupment fee equal to 25% of their total surcharges, in addition to those surcharges.

(5)	All wastewater that exceeds the limits set forth in the nondomestic user's pretreatment permit shall be surcharged for BOD, TSS and NH3 at twice the rates listed in this section. This will be in addition to the above surcharges and any penalties or fines assessed by the city for noncompliance with this chapter.

(C)	Pretreatment charges and fees. Each industrial user shall pay his proportionate share of the cost of administering the pretreatment and sampling programs and this division. The city may adopt reasonable fees for reimbursement of costs of setting up and operating the city's pretreatment program, which may include:

(1)	Fees for wastewater discharge permit applications including the cost of processing such applications;

(2)	Fees for monitoring, inspection, and surveillance procedures including the cost of collection and analyzing a user's discharge, and reviewing monitoring reports and certification statements submitted by users;

(3)	Fees for reviewing and responding to accidental discharge procedures and construction;

(4)	Fees for filing appeals;

(5)	Fees to recover administrative and legal costs (not included in division (C)(2) above) associated with the enforcement activity taken by the control authority to address industrial user noncompliance; and

(6)	Other fees as the city may deem necessary to carry out the requirements contained herein. These fees relate solely to the matters covered by this chapter and are separate from all other fees, fines, and penalties chargeable by the city.

(D)	Billings; penalty for late payment.

(1)	The combined surcharge as set forth herein shall be billed and payable monthly on a separate bill rendered to the proper person by the city's Utility Department. Failure to pay the bill within 15 days shall cause the bill to become delinquent.

2016 S-3

Sewers	63

(2)	After five days of delinquency, the city, acting through its duly authorized officers, shall disconnect the water connection serving the premises, and the water connection shall not be turned on again until the bill is paid.

(Ord. 16-04-001, passed 4-19-16)

§ 56.04  TAMPERING PROHIBITED.

(A)	It shall be unlawful to maliciously, willfully or negligently break, damage, destroy, uncover, deface or tamper with any equipment or materials belonging to the city and used for the purpose of making measurements, tests or examinations and left upon the premises of a person discharging wastes into the sewer. This protection against damage shall also apply to any part of the sewer system and wastewater treatment plant(s) and any equipment, materials or supplies used in the operation and maintenance of the facilities.

(B)	Any person violating this provision shall be subject to immediate arrest and prosecution.

(Ord. 16-04-001, passed 4-19-16)

USE REGULATIONS

§ 56.15  TESTS AND ANALYSES.

All pollutant analyses, including sampling techniques, to be submitted as part of a wastewater discharge permit application or report shall be performed in accordance with procedures established by SCDHEC and the techniques prescribed in 40 CFR Part 136 and amendments thereto, unless otherwise specified in an applicable categorical pretreatment standard. If 40 CFR Part 136 does not contain sampling or analytical techniques for the pollutant in question, or where the EPA determines that the Part 136 sampling and analytical techniques are inappropriate for the pollutant in question, sampling and analyses must be performed in accordance with procedures approved by SCDHEC and on the basis of recommendations from the state. All laboratory analyses shall be performed in a state certified laboratory. Sampling techniques must meet proper chain-of-custody procedures.

(Ord. 16-04-001, passed 4-19-16)

§ 56.16  CHARACTER AND CONCENTRATION OF WASTES.

(A)	Monitoring. The nondomestic wastewater of any person discharging the wastewater into the public sewer shall be subject to periodic inspection and a determination of the character and concentration of the wastewater. The frequency of the monitoring shall be determined by the control

2016 S-3

64	Bennettsville - Public Works

authority, based upon the industry's total wastewater load being discharged to the treatment system. The inspection and tests shall also be made immediately after any process change which might affect the quantity or quality of the wastewater being discharged.

(B)	Sample collection. Samples collected to satisfy reporting requirements must be based on data obtained through appropriate sampling and analysis performed during the period covered by the report, based on data that is representative of conditions occurring during the reporting period.

(1)	Except as indicated in divisions (2) and (3) below, the user must collect wastewater samples using 24-hour flow-proportional composite sampling techniques, unless time-proportional composite sampling or grab sampling is authorized by the control authority. Where time-proportional composite sampling or grab sampling is authorized by the city, the samples must be representative of the discharge. Using protocols (including appropriate preservation) specified in 40 CFR Part 136 and appropriate EPA guidance, multiple grab samples collected during a 24-hour period may be composited prior to the analysis as follows: for cyanide, total phenols, and sulfides the samples may be composited in the laboratory or in the field; for volatile organics and oil and grease, the samples may be composited in the laboratory. Composite samples for other parameters unaffected by the compositing procedures as documented in approved EPA methodologies may be authorized by the city, as appropriate. In addition, grab samples may be required to show compliance with instantaneous limits.

(2)	Samples for oil and grease, temperature, pH, cyanide, total phenols, sulfides, and volatile organic compounds must be obtained using grab collection techniques.

(3)	For sampling required in support of baseline monitoring and 90-day compliance reports required in § 56.42(A) and (C) [SC R.61-9.403.12(b) and (d)], a minimum of four grab samples must be used for pH, cyanide, total phenols, oil and grease, sulfide and volatile organic compounds for facilities for which historical sampling data do not exist; for facilities for which historical sampling data are available, the control authority may authorize a lower minimum. For the reports required by § 56.42(D) [SC R.61-9.403.12(e) and 403.12(h)], the industrial user is required to collect the number of grab samples necessary to assess and assure compliance by with applicable pretreatment standards and requirements.

(C)	Authority. The determination of the character and concentration of the nondomestic wastewater by the control authority shall be binding as a basis for user charges.

(D)	Cost. Total costs incident to the supervision, monitoring, sampling and analysis of wastes shall be included in the surcharge billing made to persons discharging waste into the city's sanitary sewers.

(Ord. 16-04-001, passed 4-19-16)

2016 S-3

Sewers	65

§ 56.17  MEASUREMENT OF FLOW VOLUME.

(A)	The volume of flow used in determining the total discharge of nondomestic wastewater shall be based upon:

(1)	Metered water consumption, as shown in the records of meter readings maintained by the city. If a person discharging wastewater into the public sewers produces evidence to the control authority that more than 15% of the total annual volume of water used for all purposes does not reach the public sewers, then an estimated percentage of total water consumption to be used in determining nondomestic wastewater into the public sewers based upon adequate comparison data between the actual metered wastewater discharged and metered water consumption for a relevant period of time determined by the control authority.

(2)	At the individual discharger's option, other flow measuring devices, which measure the actual volume of wastewater discharged to the sewer. The devices shall be accessibly and safely located, and the measuring system, as specified by the control authority, shall be installed in accordance with plans approved by the control authority.

(3)	The metering system shall be installed and maintained at the owner's expense.

(4)	Individual dischargers that have installed flow measuring devices to measure the actual volume of wastewater flow, shall, at the owner's expense, provide the control authority a certificate of calibration of the device(s) by a city-approved instrumentation service company and at a frequency determined by the city.

(B)	Where any person discharging wastewater to the sanitary sewer who procures all or any part of his water supply from sources other than the city, the person discharging the wastewater shall install and maintain at his expense, meters of a type approved by the control authority for the purposes of determining the proper volume of wastewater discharged to the sewers.

(Ord. 16-04-001, passed 4-19-16)

§ 56.18  STORM WATER SURFACE DRAINAGE; PROCESS AND COOLING WATERS.

(A)	No person shall discharge or cause to be discharged any storm water, surface water, uncontaminated groundwater, roof runoff or subsurface drainage, to any public sanitary sewer. The waters shall be admitted only to the sewers as are specifically designated as storm sewers or storm drains. No person shall maintain or make a connection of roof downspouts, exterior foundation drains, areaway drains or other sources of surface runoff or groundwater to a building or indirectly to a public sanitary sewer.

(B)	Unpolluted process and noncontact cooling water may, upon written application to the city and SCDHEC and approval by the control authority, be discharged to storm sewers or storm drains.

2016 S-3

66	Bennettsville - Public Works

(C)	Corrections of violations of this section shall be required with a reasonable time schedule determined by the control authority. The time schedule shall be based upon the severity of the violation and its impact upon the wastewater system.

(Ord. 16-04-001, passed 4-19-16)

§ 56.19  PROHIBITED DISCHARGE STANDARDS; SPECIAL AGREEMENTS.

(A)	General prohibitions. No user shall introduce or cause to be introduced into the POTW any pollutant or wastewater which causes pass through or interference. These general prohibitions apply to all users of the POTW whether or not they are subject to categorical pretreatment standards or any other national, state, or local pretreatment standards or requirements.

(B)	Specific prohibitions. No user shall introduce or cause or allow to be introduced into the sewer system or the wastewater treatment plant any wastewater that contains the following:

(1)	Pollutants which create a fire or explosion hazard in the POTW, including but not limited to wastestreams with a closed cup flashpoint of less than 140° F using test methods specified in 40 CFR 261.21;

(2)	Any waters or wastes having a stabilized pH lower than 5.5 or higher than 9.0, or containing heavy concentrations of salts or having other corrosive properties capable of causing damage or hazard to structures, equipment or personnel of the wastewater treatment plant;

(3)	Any ashes, cinders, sand, mud, straw, shavings, metal, glass, bones, feathers, tar, plastics, wood, paunch manure, butcher's offal or any other solid or viscous substances capable of causing obstruction to the flow in sewers or other Interference with the proper operation of the sewerage system or treatment works;

(4)	Pollutants, including oxygen-demanding pollutants (BOD, etc.), released in a discharge at a flow rate and/or pollutant concentration which, either singly or by interaction with other pollutants, will cause Interference with the POTW;

(5)	Any liquid or vapor having a temperature higher than 150° F, or 65° C, or which will inhibit biological activity in the treatment plant resulting in Interference, but in no case wastewater which causes the temperature at the introduction into the treatment plant to exceed 104 degrees F (40 degrees C);

(6)	Petroleum oil, non-biodegradable cutting oil or products of mineral oil origin in amounts that will cause interference or pass through;

(7)	Pollutants which result in the presence of toxic gases, vapors, or fumes within the POTW in a quantity that may cause acute worker health and safety problems;

2016 S-3

Sewers	67

(8)	Any trucked or hauled pollutants, except at discharge points designated by the city in accordance with § 56.47;

(9)	Any noxious or malodorous solids, liquids or gases which, either singly or by interaction with other wastes, are capable of creating a public nuisance or hazard to life or may be sufficient to prevent entry into a sewer for its maintenance or repair;

(10)	Any waters or wastes containing dyes or other color which cannot be removed by the wastewater treatment plant processes and which require specialized chemical treatment;

(11)	Any radioactive wastes or isotopes of a half-life or concentration that they do not comply with regulations or orders issued by the appropriate authority having control over their use and which will or may cause damage or hazards to the treatment works or personnel operating the system;

(12)	Any by-products, sludges, solids, rags, foam, scum, oils or greases produced from the operation of pretreatment facilities or devices;

(13)	Any materials which form excessive amounts of scum or foam that may interfere with the operation of the treatment works or cause undue additional labor in connection with its operation;

(14)	Any liquids, solids or gases which by reason of the nature or quantity are or may be sufficient either alone or by interaction with other substances to cause fire or explosion or be in any way injurious to, persons, the sewerage system, the treatment plant or the operation of the wastewater treatment plant. At no time shall two successive readings on an explosion hazard meter, at the point of discharge into the sewer system, be more than 5% nor shall any single reading exceed 10% of the lower explosive limit (LEL) of the meter, prohibited materials include but are not limited to gasoline, kerosene, naphtha, benzene, toluene, xylene, ethers, alcohols, ketones, aldehydes, peroxides, chlorates, perchlorates, bromates, carbides, hydrides and sulfides;

(15)	Any clothing, rags, textile remnants or wastes, cloth, lint, scraps, and the like, which will not pass through a one-quarter-inch mesh screen or its equivalent in screening ability;

(16)	Any waters or wastes containing syspendecL fixed, or total solids of the-character and quality that unusual attention or expense is required to handle the materials at the sewage treatment plant;

(17)	Any garbage which has not been properly shredded;

(18)	Any substance which may cause the wastewater treatment plant's effluent or any other products of the treatment plant, such as residues or sludges, to be unsuitable for reclamation, reuse and disposal, constitute a hazard to humans or animals, or to be classified a hazardous waste under state and/or federal laws and regulations;

2016 S-3

68	Bennettsville - Public Works

(19)	Any waters or wastes containing poisonous or toxic substances or any other materials in amounts exceeding standards promulgated by the Administrator of the EPA pursuant to Section 307(a) of the Clean Water Act, and chemicals or compounds which are not susceptible to treatment or which may interfere with the biological processes or efficiency of the treatment system or cause the treatment system to violate the toxicity limit in its permit, or create any hazard in the receiving stream at the wastewater treatment plant;

(20)	Any waters or wastes containing amounts of cadmium, chromium, copper, lead, nickel, zinc or other heavy metals which exceed categorical pretreatment standards, interfere with treatment efficiency or sludge disposal criteria or cause the wastewater treatment plant to exceed its NPDES permit or violate state stream standards;

(21)	Any substance which will cause the treatment works to violate its NPDES permit or its effluent to violate the water quality standards of the receiving stream;

(22)	Any wastewater at a flow rate or containing such concentrations or quantities of any given constituent that exceeds for any time period longer than 15 minutes more than five times the average 24-hour concentration, quantities or flow during normal operation and that would cause a treatment process upset and/or loss of treatment efficiency; and

(23)	Any wastewater that violates applicable categorical pretreatment standards, as promulgated by EPA in 40 CFR Parts 403 and 129, or by SCDHEC or by the city.

(C)	Conditionally prohibited discharges.

(1)	No person shall discharge or cause to be discharged the following described substances, materials, waters or wastes if it appears likely in the opinion of the control authority, that such wastes may have a deleterious effect upon the sewers, sewage treatment plant processes, equipment, or receiving waters or which otherwise may create a hazard to life, limb, property, or constitute a public nuisance. In forming his opinion as to the acceptability of these wastes, the control authority will give consideration to such factors as: quantities of subject wastes in relation to flows and velocities in the sewers, materials of construction of the sewers, nature of the sewage treatment process, capacity of the sewage treatment process, capacity of the sewage treatment plant, degree of treatability of wastes in the sewage treatment plant and other pertinent factors.

(a)	Any water or waste containing more than 100 parts per million by weight of fats, oils, grease or wax, whether emulsified or not, or containing substances which may solidify or become viscous at temperatures between 32° and 150° F, or 0° and 65° C, at the point of discharge into the system;

(b)	Any liquid wastes having a BOD concentration exceeding 250 mg/l or ppm;

2016 S-3

Sewers	69

(c)	Any liquid wastes having a TSS concentration exceeding 240 mg/l or ppm;

(d)	Any liquid wastes having a NH3 concentration exceeding 25 mg/l or ppm;

(D)	Pollutants, substances, or wastewater prohibited by this section shall not be processed or stored in such a manner that they could be discharged to the POTW.

(E)	Special agreement for discharge ofprohibited substances. No statement contained in this section shall be construed as prohibiting any special agreement or arrangement between the city and any person whereby nondomestic wastewater of unusual strength or character may be admitted into the sanitary sewers, either before or after approved pretreatment or prehandling, and specially treated subject to any payments or user charges as may be applicable, provided the wastewater will not interfere with the treatment process, sludge disposal options, NPDES permit compliance or cause a violation of water quality standards.

(Ord. 16-04-001, passed 4-19-16)

§ 56.20  NATIONAL CATEGORICAL PRETREATMENT STANDARDS.

(A)	Users must comply with the categorical pretreatment standards found at 40 CFR Chapter I, Subchapter N, Parts 405-471.

(1)	Where a categorical pretreatment standard is expressed only in terms of either the mass or the concentration of a pollutant in wastewater, the city may impose equivalent concentration or mass limits in accordance with divisions (5) and (6) below.

(2)	When the limits in a categorical pretreatment standard are expressed only in terms of mass of pollutant per unit of production, the city may convert the limits to equivalent limitations expressed either as mass of pollutant discharged per day or effluent concentration for purposes of calculating effluent limitations applicable to individual industrial users.

(3)	Combined wastestream formula. When wastewater subject to a categorical pretreatment standard is mixed with wastewater not regulated by the same standard, the city shall impose an alternate limit in accordance with SC R.61-9.403.6(f).

(4)	Net/gross adjustments. The city, at its discretion, may allow a categorical industrial user to obtain a net/gross adjustment to a categorical pretreatment standard in accordance with SC R.61-9.403.15 with the restriction that the calculated limit shall not exceed the local limit established by the city for any parameter.

(5)	Equivalent mass limits. When a categorical pretreatment standard is expressed only in terms of pollutant concentrations, an industrial user may request that the city convert the limits to equivalent

2016 S-3

70	Bennettsville - Public Works

mass limits. The determination to convert concentration limits to mass limits is within the discretion of the city. The city may establish equivalent mass limits only if the industrial user meets all the conditions set forth in SC R 61-9.403.6(d)(5).

(6)	Equivalent concentration limits. The city may convert the mass limits of the categorical pretreatment standards of 40 CFR Parts 414, 419, and 455 to concentration limits for purposes of calculating limitations applicable to individual industrial users. The conversion is at the discretion of the city.

(7)	Once included in its permit, the industrial user must comply with the equivalent limitations developed in this section in lieu of the promulgated categorical standards from which the equivalent limitations were derived.

(8)	Many categorical pretreatment standards specify one limit for calculating maximum daily discharge limitations and a second limit for calculating maximum monthly average, or four-day average, limitations. Where such standards are being applied, the same production or flow figure shall be used in calculating both the average and the maximum equivalent limitation.

(9)	Any industrial user operating under a permit incorporating equivalent mass or concentration limits calculated from a production-based standard shall notify the city within two business days after the user has a reasonable basis to know that the production level will significantly change within the next calendar month. Any user not notifying the city of such anticipated change will be required to meet the mass or concentration limits in its permit that were based on the original estimate of the long term average production rate.

(Ord. 16-04-001, passed 4-19-16)

§ 56.21  LOCAL LIMITS.

(A)	The city is authorized to establish local limits pursuant to SC R.61-9.403.5(c) and (d). Local limits are developed through the calculation of maximum allowable headworks loadings (MAHL) for all pollutants of concern as established in the pretreatment program, which is incorporated herein by reference, industrial wastewater survey information will be used to develop industrial user-specific local limits based on the mass-based allocation method. Any applicable local limits shall be included in the individual SIU or IU permit or other documents. The local limits apply at the point where the wastewater is discharged to the POTW. All concentrations for metallic substances are for total metal unless indicated otherwise. The city may impose mass limitations in addition to, or in place of, concentration-based limitations.

2016 S-3

Sewers	71

(B)	The city may develop best management practices (BMPs), by ordinance or in individual wastewater discharge permits or general permits, to implement local limits and the requirements of § 56.19.

(Ord. 16-04-001, passed 4-19-16)

§ 56.22  CITY'S RIGHT OF REVISION.

The city reserves the right to establish, by ordinance or in individual wastewater discharge permits or in general permits, more stringent standards or requirements on discharges to the POTW consistent with the purpose of this chapter.

(Ord. 16-04-001, passed 4-19-16)

§ 56.23  DILUTION.

No user shall ever increase the use of process water, or in any way attempt to dilute a discharge, as a partial or complete substitute for adequate treatment to achieve compliance with a discharge limitation unless expressly authorized by an applicable pretreatment standard or requirement. The city may impose mass limitations on users who are using dilution to meet applicable pretreatment standards or requirements, or in other cases when the imposition of mass limitations is appropriate.

(Ord. 16-04-001, passed 4-19-16)

INDUSTRIAL WASTES

§ 56.35  INDUSTRIAL WASTEWATER DISCHARGE PERMITS AND GENERAL PERMITS.

(A)	Wastewater analysis. When requested by the control authority, a user must submit information on the nature and characteristics of its wastewater within 30 days of the request. The control authority is authorized to prepare a form for this purpose and may periodically require users to update this information.

(B)	Permit required. All industrial users proposing to connect or discharge to the POTW shall obtain a wastewater discharge permit before connecting to or contributing to the POTW.

(1)	No significant industrial user shall discharge wastewater into the POTW without first obtaining an individual wastewater discharge permit or a general permit from the control authority, except that a significant industrial user that has filed a timely application pursuant to division (C) below may continue to discharge for the time period specified therein.

2016 S-3

72	Bennettsville - Public Works

(2)	The control authority may require other users to obtain individual wastewater discharge permits or general permits as necessary to carry out the purposes of this chapter.

(3)	Any violation of the terms and conditions of an individual wastewater discharge permit or a general permit shall be deemed a violation of this chapter and subjects the wastewater discharge permittee to the sanctions set out in §§ 56.63 through 56.70 and § 56.99. Obtaining an individual wastewater discharge permit or a general permit does not relieve a permittee of its obligation to comply with all federal and state pretreatment standards or requirements or with any other requirements of federal, state, and local law.

(C)	Individual wastewater discharge and general permitting: existing connections. Any user required to obtain an individual wastewater discharge permit or a general permit who was discharging wastewater into the POTW prior to the effective date of this chapter and who wishes to continue such discharges in the future, shall, within 30 days after said date, apply to the control authority for an individual wastewater discharge permit or a general permit in accordance with division (E) below.

(D)	Individual wastewater discharge and general permitting: new connections. Any user required to obtain an individual wastewater discharge permit or a general permit who proposes to begin or recommence discharging into the POTW must obtain such permit prior to the beginning or recommencing of such discharge. An application for this individual wastewater discharge permit or general permit, in accordance with division (E) below, must be filed at least 90 days prior to the date upon which any discharge will begin or recommence.

(E)	Individual wastewater discharge and general permit application contents.

(1)	All users required to obtain an individual wastewater discharge permit or a general permit must submit a permit application. Users that are eligible may request a general permit under division (F) below. The control authority may require users to submit all or some of the following information as part of a permit application:

(a)	Identifying information.

1.	The name and address of the facility, including the name of the operator and owner;

2.	Contact information, description of activities, facilities, and plant production processes on the premises.

(b)	Environmental permits. A list of any environmental control permits held by or for the facility.

2016 S-3

Sewers	73

(c)	Description of operations.

1.	A brief description of the nature, average rate of production (including each product produced by type, amount, processes, and rate of production), and standard industrial classifications of the operations) carried out by such user. This description should include a schematic process diagram, which indicates points of discharge to the POTW from the regulated processes;

2.	Types of wastes generated, and a list of all raw materials and chemicals used or stored at the facility which are, or could accidentally or intentionally be, discharged to the POTW;

3.	Number and type of employees, hours of operation, and proposed or actual hours of operation;

4.	Type and amount of raw materials processed (average and maximum per day);

5.	Site plans, floor plans, mechanical and plumbing plans, and details to show all sewers, floor drains, and appurtenances by size, location, and elevation, and all points of discharge;

(d)	Time and duration of discharges;

(e)	The location for monitoring all wastes covered by the permit;

(f)	Flow measurement. Information showing the measured average daily and maximum daily flow, in gallons per day, to the POTW from regulated process streams and other streams, as necessary, to allow use of the combined wastestream formula set out in § 56.20(A)(3) [SC R.61-9.403.6(f)].

(g)	Measurement of pollutants.

1.	The categorical pretreatment standards applicable to each regulated process and any new categorically regulated processes for existing sources.

2.	The results of sampling and analysis identifying the nature and concentration, and/or mass, where required by the standard or by the control authority, of regulated pollutants in the discharge from each regulated process.

3.	Instantaneous, daily maximum, and long-term average concentrations, or mass, where required, shall be reported.

4.	The sample shall be representative of daily operations and shall be analyzed in accordance with procedures set out in § 56.15. Where the standard requires compliance with a BMP or

2016 S-3

74	Bennettsville - Public Works

pollution prevention alternative, the user shall submit documentation as required by the control authority or the applicable standards to determine compliance with the standard.

5.	Sampling must be performed in accordance with procedures set out in § 56.16(B).

(h)	Any requests for a monitoring waiver (or a renewal of an approved monitoring waiver) for a pollutant neither present nor expected to be present in the discharge based on § 56.42(D)(2) [SC R.61-9.403.12(e)(2)].

(i)	Any request to be covered by a general permit based on division (F) below.

(j)	Any other information as may be deemed necessary by the control authority to evaluate the permit application.

(2)	Incomplete or inaccurate applications will not be processed and will be returned to the user for revision.

(F)	Wastewater discharge permitting: general permits.

(1)	At the discretion of the control authority, the control authority may use general permits to control SIU discharges to the POTW if the following conditions are met. All facilities to be covered by a general permit must:

(a)	Involve the same or substantially similar types of operations;

(b)	Discharge the same types of wastes;

(c)	Require the same effluent limitations;

(d)	Require the same or similar monitoring; and

(e)	In the opinion of the control authority are more appropriately controlled under a general permit than under individual wastewater discharge permits.

(2)	To be covered by the general permit, the SIU must file a written request for coverage that identifies its contact information, production processes, the types of wastes generated, the location for monitoring all wastes covered by the general permit, any requests in accordance with § 56.42(D)(2) for a monitoring waiver for a pollutant neither present nor expected to be present in the discharge, and any other information the POTW deems appropriate. A monitoring waiver for a pollutant neither present nor expected to be present in the discharge is not effective in the general permit until after the control authority has provided written notice to the SIU that such a waiver request has been granted in accordance with § 56.42(D)(2).

2016 S-3

Sewers	75

(3)	The control authority will retain a copy of the general permit, documentation to support the POTW's determination that a specific SIU meets the criteria in divisions (F)(l)(a) through (e) and applicable state regulations, and a copy of the user's written request for coverage for three years after the expiration of the general permit.

(4)	The control authority may not control an SIU through a general permit where the facility is subject to production-based categorical pretreatment standards or categorical pretreatment standards expressed as mass of pollutant discharged per day or for IUs whose limits are based on the combined wastestream formula (§ 56.20(A)(3)) or net/gross calculations (§ 56.20(A)(4)).

(G)	Application signatories and certifications.

(1)	All wastewater discharge permit applications, user reports and certification statements must be signed by an authorized representative of the user and contain the certification statement in § 56.42(I).

(2)	If the designation of an authorized representative is no longer accurate because a different individual or position has responsibility for the overall operation of the facility or overall responsibility for environmental matters for the company, a new written authorization satisfying the requirements of this section must be submitted to the control authority prior to or together with any reports to be signed by an authorized representative.

(3)	A facility determined to be a non-significant categorical industrial user by the control authority pursuant to § 56.01 (SIGNIFICANT INDUSTRIAL USER, division (3)) must annually submit the signed certification statement in § 56.42(I)(2).

(H)	Permit decisions. The control authority will evaluate the data furnished by the user and may require additional information. Upon determination by the control authority that a wastewater discharge permit will be issued, the limits will be developed and submitted to SCDHEC and shall only be instituted at such time as SCDHEC approval is received. The control authority may deny any application for a wastewater discharge permit.

(Ord. 16-04-001, passed 4-19-16)

§ 56.36  PERMIT ISSUANCE.

(A)	Industrial discharge permits shall be expressly subject to all provisions of this chapter and all other applicable regulations, user charges and fees established by the city. Permits may contain conditions as deemed appropriate by the control authority to ensure compliance with this chapter.

(B)	Permit duration and reissuance. An individual wastewater discharge permit or a general permit shall be issued for a specified time period, not to exceed five years from the effective date of the permit.

2016 S-3

76	Bennettsville - Public Works

An individual wastewater discharge permit or a general permit may be issued for a period less than five years, at the discretion of the control authority. Each individual wastewater discharge permit or general permit will indicate a specific date upon which it will expire. The user shall apply for permit reissuance a minimum of 180 days prior to the expiration of the user's existing permit. An individual wastewater discharge permit or general permit will remain in effect past the expiration date as long as the permittee has filed a timely application and through no fault of the permittee the POTW has not reissued the permit.

(C)	Wastewater discharge permit contents. An individual wastewater discharge permit or a general permit shall include such conditions as are deemed reasonably necessary by the control authority to prevent pass through or interference, protect the quality of the water body receiving the treatment plant's effluent, protect worker health and safety, facilitate sludge management and disposal, and protect against damage to the POTW.

(1)	Individual wastewater discharge permits and general permits must contain:

(a)	A statement that indicates the wastewater discharge permit issuance date, expiration date and effective date;

(b)	A statement that the wastewater discharge permit is nontransferable without prior notification to the city in accordance with division (E) below, and provisions for furnishing the new owner or operator with a copy of the existing wastewater discharge permit;

(c)	Effluent limits, including best management practices, based on applicable pretreatment standards;

(d)	Self-monitoring, sampling, reporting, notification, and record-keeping requirements. These requirements shall include an identification of pollutants (or best management practice) to be monitored, sampling location, sampling frequency, and sample type based on federal, state, and local law;

(e)	The process for seeking a waiver from monitoring for a pollutant neither present nor expected to be present in the discharge in accordance with § 56.42(D)(2);

(f)	A statement of applicable civil and criminal penalties for violation of pretreatment standards and requirements, and any applicable compliance schedule. Such schedule may not extend the time for compliance beyond that required by applicable federal, state, or local law;

(g)	Requirements to control slug discharge, if determined by the control authority to be necessary;

(h)	Any grant of the monitoring waiver by the control authority (§ 56.42(D)(2)) must be included as a condition in the user's permit.

2016 S-3

Sewers	77

(2)	Individual wastewater discharge permits or general permits may contain, but need not be limited to, the following conditions:

(a)	Limits on average and maximum rate and time of discharge or requirements for flow regulations and equalization;

(b)	Requirements for the installation of pretreatment technology, pollution control, or construction of appropriate containment devices, designed to reduce, eliminate, or prevent the introduction of pollutants into the treatment works;

(c)	Requirements for the development and implementation of spill control plans or other special conditions including management practices necessary to adequately prevent accidental, unanticipated, or nonroutine discharges;

(d)	Development and implementation of waste minimization plans to reduce the amount of pollutants discharged to the POTW;

(e)	 The unit charge or schedule of user charges and fees for the management of the wastewater discharged to the POTW;

(f)	Requirements for installation and maintenance of inspection and sampling facilities and equipment, including flow measurement devices;

(g)	A statement that compliance with the wastewater discharge permit does not relieve the permittee of responsibility for compliance with all applicable federal and state pretreatment standards, including those which become effective during the term of the wastewater discharge permit;

(h)	Other conditions as deemed appropriate by the city to ensure compliance with this chapter, and state and federal laws, rules, and regulations.

(D)	Permit modification. The terms and conditions of the wastewater discharge permit may be subject to modification by the city during the term of the permit as limitations or requirements as identified in this chapter are modified or other just cause exists. The user shall be informed of any proposed changes in the permit at least 30 days prior to the effective date of change. Any changes or new conditions in the permit shall include a reasonable time schedule for compliance.

(1)	The control authority may modify an individual wastewater discharge permit for good cause, including, but not limited to, the following reasons:

(a)	To incorporate any new or revised federal, state, or local pretreatment standards or requirements;

2016 S-3

78	Bennettsville - Public Works

(b)	To address significant alterations or additions to the user's operation, processes, or wastewater volume or character since the time of the individual wastewater discharge permit issuance;

(c)	A change in the POTW that requires either a temporary or permanent reduction or elimination of the authorized discharge;

(d)	Information indicating that the permitted discharge poses a threat to the city's POTW or beneficial sludge use, city personnel, or the receiving waters;

(e)	Violation of any terms or conditions of the individual wastewater discharge permit;

(f)	Misrepresentations or failure to fully disclose all relevant facts in the wastewater discharge permit application or in any required reporting;

(g)	Revision of or a grant of variance from categorical pretreatment standards pursuant to SC R.61-9.403.13;

(h)	To correct typographical or other errors in the individual wastewater discharge permit; or

(i)	To reflect a transfer of the facility ownership or operation to a new owner or operator where requested in accordance with division (E) below.

(2)	The control authority may modify a general permit for good cause, including, but not limited to, the following reasons:

(a)	To incorporate any new or revised federal, state, or local pretreatment standards or requirements;

(b)	A change in the POTW that requires either a temporary or permanent reduction or elimination of the authorized discharge;

(c)	To correct typographical or other errors in the individual wastewater discharge permit; or

(d)	To reflect a transfer of the facility ownership or operation to a new owner or operator where requested in accordance with division (E) below.

(E)	Wastewater discharge permit transfer. Wastewater discharge permits are issued to a specific person for a specific operation. A wastewater discharge permit shall not be reassigned or transferred or sold to a new owner, new user, different premises or a new or changed operation without the approval of the city. Any succeeding owner or user shall also comply with the terms and conditions of the existing

2016 S-3

Sewers	79

permit. Individual wastewater discharge permits or coverage under general permits may be transferred to a new owner or operator only if the permittee gives at least 30 days advance notice to the control authority and the city approves the individual wastewater discharge permit or the general permit coverage transfer. The notice must include a written certification by the new owner or operator which:

(1)	States that the new owner and/or operator has no immediate intent to change the facility's operations and processes;

(2)	Identifies the specific date on which the transfer is to occur; and

(3)	Acknowledges full responsibility for complying with the existing individual wastewater discharge permit or general permit.

Failure to provide advance notice of a transfer renders the individual wastewater discharge permit or coverage under the general permit void as of the date of facility transfer.

(F)	Individual wastewater discharge permit and general permit revocation. Any person who violates the conditions of his permit, of this division or of applicable state and federal regulations is subject to having his permit revoked. Violations subjecting a user to possible revocation of his permit include, but are not limited to, the following:

(1)	Failure to notify the control authority of significant changes to the wastewater prior to the changed discharge;

(2)	 Failure to provide prior notification to the control authority of changed conditions pursuant to § 56.46(B);

(3)	Misrepresentation or failure to fully disclose all relevant facts in the wastewater discharge permit application;

(4)	Falsifying self-monitoring reports and certification statements;

(5)	Tampering with monitoring equipment;

(6)	Refusing to allow the control authority timely access to the facility premises and records;

(7)	Failure to meet effluent limitations;

(8)	Failure to pay fines;

(9)	Failure to pay sewer charges;

2016 S-3

80	Bennettsville - Public Works

(10)	Failure to meet compliance schedules;

(11)	Failure to complete a wastewater survey or the wastewater discharge permit application;

(12)	Failure to provide advance notice of the transfer of business ownership of a permitted facility; or

(13)	Violation of any pretreatment standard or requirement, or any terms of the wastewater discharge permit or the general permit or this chapter.

(G)	Individual wastewater discharge permits or coverage under general permits shall be voidable upon cessation of operations or transfer of business ownership. All individual wastewater discharge permits or general permits issued to a user are void upon the issuance of a new individual wastewater discharge permit or a general permit to that user.

(Ord. 16-04-001, passed 4-19-16)

§ 56.37  CHARACTERISTICS OF WATERS OR WASTES; FLOW.

(A)	Any waters or wastes discharged by any person which have the characteristics prohibited in § 56.19(C) may be admitted into the sanitary sewers conditionally through issuance of a permit to discharge.

(B)	Waters or waste discharged by any person, which have an average working day flow greater than 5,000 gallons may be admitted into the sanitary sewers. The waters or wastes are discharged at the rates which will not overload the respective pumping stations, gravity sewers or treatment plant. In case of hydraulic overloads, the owner may be required to control the rates of discharge so as to prevent overloads.

(C)	Where the volume of any waters or waste discharged by any person exceeds the limits set forth under § 56.19(C), the entire volume of waste shall be understood to come within the limitations set forth under this section.

(Ord. 16-04-001, passed 4-19-16)

§ 56.38  PRELIMINARY TREATMENT OR HANDLING.

(A)	Pretreatment facilities.

(1)	Users shall provide wastewater treatment as necessary to comply with this chapter and shall achieve compliance with all categorical pretreatment standards, local limits, and the prohibitions set out

2016 S-3

Sewers	81

in § 56.19 within the time limitations specified by EPA, the state, or city, whichever is more stringent. Any facilities necessary for compliance shall be provided, operated, and maintained at the user's expense.

(a)	Plans, specifications and other pertinent information relating to proposed preliminary treatment or handling facilities shall be submitted for the approval of the control authority and no construction of the facilities shall be commenced until approval is obtained in writing. The review of such plans and operating procedures shall in no way relieve the user from the responsibility of modifying such facilities as necessary to produce a discharge acceptable to the city under the provisions of this chapter.

(b)	A permit to construct any pretreatment facilities must also be obtained from SCDHEC.

(2)	The facilities shall be constructed in accordance with a compliance schedule submitted by the person and approved by the control authority and within the time limitations as may be specified by EPA, if applicable.

(3)	The city and SCDHEC may require that any pretreatment facility be operated and maintained by a certified wastewater treatment operator. The operator must have a valid operator's certification issued by S.C. ECB at the level of certification required by SCDHEC for that facility.

(B)	Additional pretreatment measures.

(1)	Whenever deemed necessary, the control authority may require users to restrict their discharge during peak flow periods, designate that certain wastewater be discharged only into specific sewers, relocate and/or consolidate points of discharge, separate sewage wastestreams from industrial wastestreams, and such other conditions as may be necessary to protect the POTW and determine the user's compliance with the requirements of this chapter.

(2)	The control authority may require any person discharging into the POTW to install and maintain, on their property and at their expense, a suitable storage and flow-control facility to ensure equalization of flow. An individual wastewater discharge permit or a general permit may be issued solely for flow equalization.

(3)	Grease, oil and sand interceptors shall be provided when, in the opinion of the control authority, they are necessary for the proper handling and control of liquid wastes containing grease, oil, and sand in excessive amounts. Interceptors shall not be required for private living quarters or dwelling units but may be required for industrial or commercial establishments, public eating places, hospitals, hotels, abattoirs or other institutions. All interception units shall be of a type and capacity approved by the control authority, in accordance with § 56.48.

2016 S-3

82	Bennettsville - Public Works

(4)	All interceptors shall be located so as to bo readily accessible for cleaning and inspection and shall be supplied and properly maintained and continuously in satisfactory and effective operation, by the owner at his expense, in accordance with § 56.48.

(5)	Users with the potential to discharge flammable substances may be required to install and maintain an approved combustible gas detection meter.

(C)	Accidental discharge/slug discharge control plans. The control authority shall evaluate whether each SIU needs an accidental discharge/slug discharge control plan or other action to control slug discharges. The control authority may require any user to develop, submit for approval, and implement such a plan or take such other action that may be necessary to control slug discharges. Alternatively, the control authority may develop such a plan for any user. An accidental discharge/slug discharge control plan shall address, at a minimum, the following:

(1)	Description of discharge practices, including nonroutine batch discharges;

(2)	Description of stored chemicals;

(3)	Procedures for immediately notifying the POTW of any accidental or slug discharge, as required by § 56.46(C); and

(4)	Procedures to prevent adverse impact from any accidental or slug discharge. Such procedures include, but are not limited to, inspection and maintenance of storage areas, handling and transfer of materials, loading and unloading operations, control of plant site runoff, worker training, building of containment structures or equipment, measures for containing toxic organic pollutants, including solvents, and/or measures and equipment for emergency response.

(D)	Any person discharging industrial wastes into the public sewers may be required to construct and maintain a suitable control or inspection manhole either downstream from any treatment, storage or other approved works or, if pretreatment is not required, at the point where the wastes enter the public sewers.

(E)	All new significant industrial users proposing to connect to or discharge into any parts of the wastewater treatment system shall install a suitable control and inspection manhole with a primary flow measuring device as approved by the control authority.

(F)	The manhole shall be located so as to be readily accessible and shall be constructed in such a manner as may be approved by the control authority to facilitate inspection or measuring which may be necessary for proper sampling or control of the waste discharged.

(Ord. 16-04-001, passed 4-19-16)

2016 S-3

Sewers	83

§ 56.39  CONTROL OF PROHIBITED WASTES.

If wastewater containing any substance described in § 56.19(C) is discharged or proposed to be discharged into the sewer system of the city, the control authority may take action necessary to:

(A)	Prohibit the discharge of the wastewater;

(B)	Require a discharger to demonstrate that in-plant modifications will reduce or eliminate the discharge of the substances in conformity with this division;

(C)	Require pretreatment, including equalization facilities, necessary to reduce or eliminate the objectionable characteristics or substances so that the discharge will not violate these rules or regulations;

(D)	Require the person making, causing or allowing the discharge to pay any additional cost or expense incurred by the city for handling and treating excess loads imposed on the treatment system; and

(E)	Take other remedial action as may be necessary to achieve the purpose of this division.

(Ord. 16-04-001, passed 4-19-16)

§ 56.40  ACCIDENTAL DISCHARGE; TREATMENT BYPASSES.

(A)	(1)	Each industrial user shall provide protection from accidental discharge of prohibited materials or other wastewater regulated by this division.

(2)	Facilities to prevent accidental discharge of prohibited materials or other wastewater regulated by this division shall be provided and maintained at the owner's cost and expense.

(B)	A bypass of the user's treatment system is prohibited, and the control authority may take enforcement action against a user for a bypass, unless all of the following conditions are met:

(1)	The bypass was unavoidable to prevent loss of life, personal injury or severe property damage;

(2)	There were no feasible alternatives to the bypass, such as the use of auxiliary treatment facilities, retention of untreated wastes, or maintenance during normal periods of equipment downtime. This condition is not satisfied if adequate back-up equipment should have been installed in the exercise of reasonable engineering judgment to prevent a bypass which occurred during normal periods of equipment downtime or preventive maintenance; and

(3)	The user properly notified the control authority or his designee, described in § 56.41(C).

2016 S-3

84	Bennettsville - Public Works

(C)	Advance notice of bypass. A user may allow a bypass to occur which does not cause pretreatment standards or requirements to be violated, but only if it is for essential maintenance to ensure efficient operation of the treatment system. Users anticipating a bypass shall submit notice to the control authority at least ten days in advance. The control authority may only approve the anticipated bypass if the circumstances satisfy those set forth in § 56.40(B).

(Ord. 16-04-001, passed 4-19-16)

§ 56.41  NONCOMPLIANCE; REPORTING.

(A)	If for any reason a facility does not comply with or will not be able to comply with any prohibition or limitations of this division, the facility responsible for the discharge shall immediately notify the control authority so corrective action may be taken to protect the treatment system.

(B)	If the sampling performed by a significant industrial user indicates a violation of his permit, the user must notify the control authority within 24 hours of becoming aware of the violation. The user shall also repeat the sampling and analysis and submit the results of the repeat analysis within 30 days after becoming aware of the violation.

(C)	Unanticipated bypass. A user shall submit oral notice to the control authority of an unanticipated bypass that exceeds applicable pretreatment standards within 24 hours from the time it becomes aware of the bypass. A written submission shall also be provided within five days of the time the user becomes aware of the bypass. The written submission shall contain a description of the bypass and its cause; the duration of the bypass, including exact dates and times, and, if the bypass has not been corrected, the anticipated time it is expected to continue; and steps taken or planned to reduce, eliminate, and prevent reoccurrence of the bypass. The control authority may waive the written report on a case-by-case basis if the oral report has been received within 24 hours.

(Ord. 16-04-001, passed 4-19-16)

§ 56.42  REPORTING REQUIREMENTS.

(A)	Baseline monitoring reports.

(1)	Within either 180 days after the effective date of a categorical pretreatment standard, or the final administrative decision on a category determination under SC R.61-9.403.6(b)(4), whichever is later, existing categorical industrial users currently discharging to or scheduled to discharge to the POTW shall submit to the control authority a report which contains the information listed in division (A)(2), below. At least 90 days prior to commencement of their discharge, new sources, and sources that become categorical industrial users subsequent to the promulgation of an applicable categorical standard, shall submit to the control authority a report which contains the information listed in division

2016 S-3

Sewers	85

(A)(2), below. A new source shall report the method of pretreatment it intends to use to meet applicable categorical standards. A new source also shall give estimates of its anticipated flow and quantity of pollutants to be discharged.

(2)	Users described above shall submit the information set forth below.

(a)	All information required in §§ 56.35(E)(1)(a)1., 56.35(E)(1)(b), 56.35(E)(1)(c)1. and  56.35(E)(1)(f).

(b)	Measurement of pollutants.

1.	The user shall provide the information required in §56.35(E)(1)(g)1. through 4.

2.	The user shall take a minimum of one representative sample to compile that data necessary to comply with the requirements of this division.

3.	Samples should be taken immediately downstream from pretreatment facilities if such exist or immediately downstream from the regulated process if no pretreatment exists. If other wastewaters are mixed with the regulated wastewater prior to pretreatment the user should measure the flows and concentrations necessary to allow use of the combined wastestream formula in SC R.61-9.403.6(f) to evaluate compliance with the pretreatment standards. Where an alternate concentration or mass limit has been calculated in accordance with SC R.61-9.40 CFR 403.6(f) this adjusted limit along with supporting data shall be submitted to the city.

4.	Sampling and analysis shall be performed in accordance with § 56.15.

5.	The control authority may allow the submission of a baseline report which utilizes only historical data so long as the data provides information sufficient to determine the need for industrial pretreatment measures.

6.	The baseline report shall indicate the time, date and place of sampling and methods of analysis, and shall certify that such sampling and analysis is representative of normal work cycles and expected pollutant discharges to the POTW.

(c)	Compliance certification. A statement, reviewed by the user's authorized representative, as defined in § 56.01, and certified by a qualified professional, indicating whether pretreatment standards are being met on a consistent basis, and, if not, whether additional operation and maintenance (O&M) and/or additional pretreatment is required to meet the pretreatment standards and requirements.

(d)	Compliance schedule. If additional pretreatment and/or O&M will be required to meet the pretreatment standards, the shortcut schedule by which the user will provide such additional

2016 S-3

86	Bennettsville - Public Works

pretreatment and/or O&M must be provided. The completion date in this schedule shall not be later than the compliance date established for the applicable pretreatment standard. A compliance schedule pursuant to this section must meet the requirements set out in division (B) below.

(e)	Signature and report certification. All baseline monitoring reports must be certified in accordance with division (I) below and signed by an authorized representative, as defined in § 56.01.

(B)	Compliance schedule progress reports. The following conditions shall apply to the compliance schedule required by division (A)(2)(d) above:

(1)	The schedule shall contain progress increments in the form of dates for the commencement and completion of major events leading to the construction and operation of additional pretreatment required for the user to meet the applicable pretreatment standards (such events include, but are not limited to, hiring an engineer, completing preliminary and final plans, executing contracts for major components, commencing and completing construction, and beginning and conducting routine operation);

(2)	No increment referred to above shall exceed nine months;

(3)	The user shall submit a progress report to the control authority no later than 14 days following each date in the schedule and the final date of compliance including, as a minimum, whether or not it complied with the increment of progress, the reason for any delay, and, if appropriate, the steps being taken by the user to return to the established schedule; and

(4)	In no event shall more than nine months elapse between such progress reports to the control authority.

(C)	Reports on compliance with categorical pretreatment standard deadline. Within 90 days following the date for final compliance with applicable categorical pretreatment standards, or in the case of a new source following commencement of the introduction of wastewater into the POTW, any user subject to such pretreatment standards and requirements shall submit to the control authority a report containing the information described in § 56.35(E)(1)(f) and (g) and division (A)(2)(b) above. For users subject to equivalent mass or concentration limits established in accordance with the procedures in 40 CFR 403.6(c), this report shall contain a reasonable measure of the user's long-term production rate. For all other users subject to categorical pretreatment standards expressed in terms of allowable pollutant discharge per unit of production (or other measure of operation), this report shall include the user's actual production during the appropriate sampling period. All compliance reports must be signed and certified in accordance with division (I)(1) below. All sampling will be done in conformance with § 56.16(B).

(D)	Periodic compliance reports.

(1)	Except as specified in division (D)(3) below, all significant industrial users must, at a frequency determined by the control authority, submit no less than twice per year (June and December

2016 S-3

Sewers	87

or on dates specified) reports indicating the nature, concentration of pollutants in the discharge which are limited by pretreatment standards and the measured or estimated average and maximum daily flows for the reporting period. In cases where the pretreatment standard requires compliance with a best management practice (BMP) or pollution prevention alternative, the user must submit documentation required by the control authority or the pretreatment standard necessary to determine the compliance status of the user. All laboratory analyses shall be performed in a state certified laboratory. Self-monitoring reports must be accompanied by all chain of custody sheets and laboratory data results for each sampling occurrence.

(2)	Waiver for pollutant not present. The city, at its discretion, may authorize an industrial user subject to a categorical pretreatment standard to forego sampling of a pollutant regulated by a categorical pretreatment standard if the industrial user has demonstrated through sampling and other technical factors that the pollutant is neither present nor expected to be present in the discharge, or is present only at background levels from intake water and without any increase in the pollutant due to activities of the industrial user. This authorization is subject to the conditions set forth in SC R.61-9.403.12(e)(2). The request for a monitoring waiver must be signed by a duly authorized representative of the user, and include the certification statement in division (I)(1) below.

(3)	Reduced reporting.

(a)	The city, at its discretion, may reduce the requirement for periodic compliance reports [(see division (1) above) (SC R 61-9.403.12(e)(3))] to a requirement to report no less frequently than once a year, unless required more frequently in the pretreatment standard or by the state, where the industrial user's total categorical wastewater flow does not exceed any of the following:

1.	0.01% of the POTW's design dry-weather hydraulic capacity of the POTW, or 5,000 gallons per day, whichever is smaller, as measured by a continuous effluent flow monitoring device unless the industrial user discharges in batches;

2.	0.01% of the design dry-weather organic treatment capacity of the POTW; and

3.	0.01% of the maximum allowable headworks loading for any pollutant regulated by the applicable categorical pretreatment standard for which approved local limits were developed in accordance with § 56.21.

(b)	Reduced reporting is not available to industrial users that have in the last two years been in significant noncompliance, as defined in § 56.70. In addition, reduced reporting is not available to an industrial user with daily flow rates, production levels, or pollutant levels that vary so significantly that, in the opinion of the control authority, decreasing the reporting requirement for this industrial user would result in data that are not representative of conditions occurring during the reporting period.

2016 S-3

88	Bennettsville - Public Works

(4)	All periodic compliance reports must be signed and certified in accordance with division (I)(1) below.

(5)	All wastewater samples must be representative of the user's discharge. Wastewater monitoring and flow measurement facilities shall be properly operated, kept clean, and maintained in good working order at all times. The failure of a user to keep its monitoring facility in good working order shall not be grounds for the user to claim that sample results are unrepresentative of its discharge.

(6)	If a user subject to the reporting requirement in this section monitors any regulated pollutant at the appropriate sampling location more frequently than required by the control authority, using the procedures prescribed in § 56.16(B), the results of this monitoring shall be included in the report.

(7)	Users that send electronic (digital) documents to the city to satisfy the requirements of this section must:

(a)	Satisfy the requirements of 40 CFR Part 3 - (electronic reporting);

(b)	For any documents submitted electronically, submit duplicate hard copies in accordance with the provisions of this section.

(E)	Reports from unpermitted users. All users not required to obtain an individual wastewater discharge permit or general permit shall provide appropriate reports to the control authority as the control authority may require.

(F)	Notice of violation/repeat sampling and reporting. If sampling performed by a user indicates a violation, the user must notify the control authority within 24 hours of becoming aware of the violation. The user shall also repeat the sampling and analysis and submit the results of the repeat analysis to the control authority within 30 days after becoming aware of the violation. Resampling by the industrial user is not required if the city performs sampling at the user's facility at least once a month, or if the city performs sampling at the user between the time when the initial sampling was conducted and the time when the user or the city receives the results of this sampling, or if the city has performed the sampling and analysis in lieu of the industrial user.

(G)	Notification of the discharge of hazardous waste. The discharge of hazardous waste into the POTW is hereby prohibited.

(H)	Date of receipt of reports. Written reports will be deemed to have been submitted on the date postmarked. For reports, which are not mailed, postage prepaid, into a mail facility serviced by the United States Postal Service, the date of receipt ofthe report shall govern.

2016 S-3

Sewers	89

(I)	Certification statements.

(1)	Certification of permit applications. The following certification statement is required to be signed and submitted by users submitting permit applications in accordance with § 56.35(G); users submitting baseline monitoring reports under division (A)(2)(e) above; users submitting reports on compliance with the categorical pretreatment standard deadlines under division (C) above; users submitting periodic compliance reports required by division (D)(1) through (4) above, and users submitting an initial request to forego sampling of a pollutant on the basis of division (D)(2) above. The following certification statement must be signed by an authorized representative, as defined in §56.01:

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gather and evaluate the information submitted. Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete. I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations.

(2)	Annual certification for non-significant categorical industrial users. A facility determined to be a non-significant categorical industrial user by the control authority pursuant to § 56.01 (SIGNIFICANT INDUSTRIAL USER, division (3)) and § 56.35(G)(3) must annually submit the following certification statement signed in accordance with the signatory requirements in § 56.01. This certification must accompany an alternative report required by the control authority:

Based on my inquiry of the person or persons directly responsible for managing compliance with the categorical Pretreatment Standards under 40 CFR        , I certify that, to the best of my knowledge and belief that during the period from                                              [months, days, year]:

(a)	The facility described as                                 [facility name] met the definition of a non-significant categorical industrial user as described in § 56.01 (SIGNIFICANT INDUSTRIAL USER, division (3));

(b)	The facility complied with all applicable pretreatment standards and requirements during this reporting period; and

(c)	The facility never discharged more than 100 gallons of total categorical wastewater on any given day during this reporting period.

This compliance certification is based on the following information.

2016 S-3

90	Bennettsville - Public Works

(3)	Certification of pollutants not present. Users that have an approved monitoring waiver based on division (D)(2) above must certify on each report with the following statement that there has been no increase in the pollutant in its wastestream due to activities of the user.

Based on my inquiry of the person or persons directly responsible for managing compliance with the pretreatment standard for 40 CFR                         [specify applicable National Pretreatment Standard part(s)], I certify that, to the best of my knowledge and belief, there has been no increase in the level of                                 [list pollutants] in the wastewaters due to the activities at the facility since filing of the last periodic report under § 56.42(D)(1).

(Ord. 16-04-001, passed 4-19-16)

§ 56.43  RECORDS RETENTION.

Users subject to the reporting requirements of this chapter shall retain, and make available for inspection and copying, all records of information obtained pursuant to any monitoring activities required by this chapter, any additional records of information obtained pursuant to monitoring activities undertaken by the user independent of such requirements, and documentation associated with best management practices established under § 56.21(B). Records shall include the date, exact place, method, and time of sampling, and the name of the person(s) taking the samples; the dates analyses were performed; who performed the analyses; the analytical techniques or methods used; and the results of such analyses. These records shall remain available for a period of at least three years. This period shall be automatically extended for the duration of any litigation concerning the user or the city, or where the user has been specifically notified of a longer retention period by the control authority.

(Ord. 16-04-001, passed 4-19-16)

§ 56.44  CONFIDENTIAL INFORMATION.

(A)	Information and data on a user obtained from reports, questionnaires, permit applications, permits, monitoring programs and from inspections and sampling activities shall be available to the public or other governmental agencies without restriction unless the user specifically requests and is able to demonstrate to the satisfaction of the city that the release of such information would divulge information, processes or methods of production entitled to protection as trade secrets under applicable state law. Any such request must be asserted at the time of submission of the information or data. When requested and demonstrated by the user furnishing a report that such information should be held confidential, the portions of a report which might disclose trade secrets or secret processes shall not be made available for inspection by the public, but shall be made available immediately upon request to governmental agencies for uses related to the NPDES program or pretreatment program, and in enforcement proceedings involving the person furnishing the report.

2016 S-3

Sewers	91

(B)	Wastewater constituents and characteristics and other effluent data, as defined at 40 CFR 2.302 shall not be recognized as confidential information and shall be available to the public without restriction.

(Ord. 16-04-001, passed 4-19-16)

§ 56.45  MAXIMUM RESTRICTIONS.

In the event that effluent standards and limitations specified in this chapter, and categorical pretreatment standards, or other EPA or SCDHEC standards both apply, the most stringent or restrictive shall become applicable.

(Ord. 16-04-001, passed 4-19-16)

§ 56.46  DISCHARGES; DISRUPTED SERVICE.

(A)	Notice shall be given to the City Administrator or his designee when wastewater will not be available for discharge, for a period of 12 hours or longer, or when a change of process is contemplated or malfunction of the pretreatment facility occurs or is anticipated which will alter demands on the wastewater treatment system. Normal operations shall include allowances for legal holidays and other announced plant shutdown.

(B)	Reports of changed conditions. Each user must notify the control authority of any significant changes to the user's operations or system which might alter the nature, quality, or volume of its wastewater at least 30 days before the change.

(1)	The control authority may require the user to submit such information as may be deemed necessary to evaluate the changed condition, including the submission of a complete wastewater analysis and wastewater discharge permit application under § 56.35(E), at no cost to the city.

(2)	The control authority may issue an individual wastewater discharge permit or a general permit under § 56.36(B) or modify an existing wastewater discharge permit or a general permit under § 56.36(D) in response to changed conditions or anticipated changed conditions.

(C)	Reports of potential problems.

(1)	In the case of any discharge, including, but not limited to, accidental discharges, discharges of a nonroutine, episodic nature, a noncustomary batch discharge, a slug discharge or slug load, that might cause potential problems for the POTW, the user shall immediately telephone and notify the control authority of the incident. This notification shall include the location of the discharge, type of waste, concentration and volume, if known, and corrective actions taken by the user.

2016 S-3

92	Bennettsville - Public Works

(2)	Within five days following such discharge, the user shall, unless waived by the control authority, submit a detailed written report describing the cause(s) of the discharge and the measures to be taken by the user to prevent similar future occurrences. Such notification shall not relieve the user or any expense, loss, damage, or other liability which might be incurred as a result of damage to the POTW, natural resources, or any other damage to person or property; nor shall such notification relieve the user of any fines, penalties, or other liability which may be imposed pursuant to this chapter.

(3)	A notice shall be permanently posted on the user's bulletin board or other prominent place advising employees who to call in the event of a discharge described in division (C)(1), above. Employers shall ensure that all employees, who could cause such a discharge to occur, are advised of the emergency notification procedure.

(4)	Significant industrial users are required to notify the control authority immediately of any changes at its facility affecting the potential for a slug discharge.

(Ord. 16-04-001, passed 4-19-16)

§ 56.47  SEPTAGE WASTES.

(A)	Persons desiring to discharge septage wastes into the wastewater treatment plant shall be required to obtain a permit from the city. A permit shall be purchased from the city at a fee set by the city and shall be valid for one year. The fee for the septage discharge permit is $25.

(B)	The discharge of septage wastes will be subject to prepayment of fees or charges fixed by the city based upon the full capacity of each vehicle for each discharge. The city reserves the right to base charges upon the concentrations of pollutants contained in the wastes of each load in addition to, or in lieu of a volume based fee. The discharge fee for each load is $10 per 1,000 gallons, or any portion thereof, of vehicle tank capacity.

(C)	The city will issue no refund for unused pre-purchased discharge tickets.

(D)	Septage will only be accepted at the wastewater treatment plant during posted business hours.

(E)	The applicant shall be the owner ofthe vehicle for which a permit is applied. Any false, untruthful, or misleading statements in any application for a permit or in any paper submitted in support of the application will invalidate the permit. A permit may be suspended or revoked at any time by the city for willful, continued or persistent violations of these rules and regulations or upon other grounds as the control authority deems proper.

(F)	All equipment (trucks, tanks, pumps and hoses) used for the collection or transportation of septage wastes shall be modem equipment in good repair. When more than one vehicle is used by any applicant, each vehicle shall bear an identifying number. The city shall refuse a permit to any person utilizing equipment other than above.

2016 S-3

Sewers	93

(G)	All applicants for a permit shall furnish the following information with each application:

(1)	Name and address of applicant;

(2)	Volume of septage waste for each numbered vehicle; and

(3)	Number of septage vehicles in collection service.

(H)	Septage wastes shall be as defined by this chapter. At no time will the disposal of hazardous wastes or other materials or wastes prohibited be allowed into the wastewater treatment system. All septage wastes shall be subject to the requirements herein.

(I)	Septage shall in no case be held or stored by the hauler for longer than 64 hours prior to discharge at the wastewater treatment plant All septage stored or held over 16 hours shall be aerated continuously while in storage.

(J)	It is unlawful to discharge, or cause to be discharged, any septage wastes into the sewer system at any point not designated in writing by the control authority.

(Ord. 16-04-001, passed 4-19-16)  Penalty, see § 56.99

§ 56.48  GREASE TRAPS.

(A)	(1)	All commercial and/or industrial entities that are involved in the preparation and/or serving of food shall install and maintain a grease trap in the sewer line(s) serving the establishment to meet the limits established in § 56.19(C).

(2)	All traps shall be of a design approved by the control authority and easily accessible for inspecting purposes.

(B)	The City Administrator shall designate an individual responsible for the inspection of these grease traps. This person will develop a procedure and format for these inspections to determine the proper operation of the grease traps.

(C)	All grease traps are subject to inspection at least twice yearly on a scheduled basis. Additionally, the city may perform at least two unannounced inspections of each grease trap per year.

(D)	The owner of each grease trap that fails to pass the inspection will be fined $100 for the first failure. A second failure to pass an inspection will result in a $500 fine.

(E)	The third failure to pass an inspection will result in the city having the trap maintained at the owner's expense for a year.

2016 S-3

94	Bennettsville - Public Works

(F)	Failure of the owner to make payment to the city for the expense of mamtaining his grease trap within the allotted time will result in the termination of water and sewer services to the establishment.

(G)	Existing commercial entities subject to § 56.63(A) may be granted a waiver by the control authority upon submission and implementation of an approved oil and grease management plan that significantly reduces the amount of oil and grease entering the sewer system from the commercial entity.

(Ord. 16-04-001, passed 4-19-16)

ADMINISTRATION AND ENFORCEMENT

§ 56.60  PERMIT CONDITIONS.

(A) The control authority may enforce whatever limits deemed necessary to protect the sanitary sewerage system and the waste treatment facilities or to facilitate the operation of the sanitary sewerage system and the waste treatment facilities.

(B)	The control authority may adjust or revise permit limitations as needed to protect the sanitary sewerage system and the waste treatment facilities or to facilitate the operation of the sanitary sewerage system and the waste treatment facilities, in accordance with § 56.36(D).

(C)	The City Council may set limits on toxic and priority pollutants that are more stringent than state and federal requirements when it is necessary for the protection of the sewerage system and/or the proper operation of the waste treatment facilities, in accordance with § 56.22.

(D)	The City Council may exclude from the sanitary sewerage system any industrial waste or other pollutant, whether pretreated or not, whenever in the opinion of the City Council, the action is necessary to protect the sanitary sewerage system and the waste treatment facilities or to facilitate the operation of the sanitary sewerage system and the waste treatment facilities.

(E)	Federal and state requirements and limitations on discharges shall apply in any case where they are more stringent than requirements and limitations as set forth in this chapter.

(Ord. 16-04-001, passed 4-19-16)

§ 56.61  PRETREATMENT PROGRAM SURVEILLANCE.

Annual inspection and sampling. The authority will conduct at a minimum annually, overall compliance inspections of all significant industrial users. The inspection will include a review of the following requirements:

2016 S-3

Sewers	95

(A) Sampling and analysis of effluent discharges;

(B) Record keeping;

(C)	All chemical inventories of raw materials or chemicals stored onsite;

(D)	Evaluation of production operations;

(E)	Evaluation of pretreatment facilities:

(1) Operation;

(2) Design;

(3) Maintenance;

(4) Sampling methods;

(5) Analytical techniques;

(6)	Flow measurement; and

(7)	Any other area designated by the control authority.

(Ord. 16-04-001, passed 4-19-16)

§ 56.62  INSPECTIONS; AUTHORITY.

(A)	Right of entry; inspection and sampling. The control authority and duly authorized representatives of the city shall have the right to enter the premises of any user to determine whether the user is complying with all requirements of this chapter and any individual wastewater discharge permit or general permit or order issued hereunder. Users shall allow the control authority ready access to all parts of the premises for the purposes of inspection, sampling, records examination and copying, and the performance of any additional duties. The city shall notify, if available, the person or a representative of the person prior to entering the premises.

(1)	 Where a user has security measures in force which require proper identification and clearance before entry into its premises, the user shall make necessary arrangements with its security guards so that, upon presentation of suitable identification, the control authority shall be permitted to enter without delay for the purposes of performing specific responsibilities.

2016 S-3

96	Bennettsville - Public Works

(2)	The control authority shall have the right to set up on the user's property, or require installation of, such devices as are necessary to conduct sampling and/or metering of the user's operations.

(3)	The control authority may require the user to install monitoring equipment as necessary. The facility's sampling and monitoring equipment shall be maintained at all times in a safe and proper operating condition by the user at its own expense. All devices used to measure wastewater flow and quality shall be calibrated once per year to ensure their accuracy.

(4)	Any temporary or permanent obstruction to safe and easy access to the facility to be inspected and/or sampled shall be promptly removed by the user at the written or verbal request of the control authority and shall not be replaced. The costs of clearing such access shall be borne by the user.

(5)	Unreasonable delays in allowing the control authority access to the user's premises shall be a violation of this chapter.

(B)	Each significant industrial user shall be subject to a facility inspection each year to review production processes and pretreatment facilities.

(Ord. 16-04-001, passed 4-19-16)

§ 56.63  NOTIFICATION OF VIOLATIONS; NUISANCES.

(A)	When the control authority finds that a user has violated, or continues to violate, any provision of this chapter, a wastewater discharge permit, or order issued hereunder, or any other pretreatment standard or requirement, the control authority may serve upon that user a written notice of violation. Within the time limit specified in the notice of violation, an explanation of the violation and a plan for the satisfactory correction and prevention thereof, to include specific required actions, shall be submitted by the user to the control authority. Submission of such a plan in no way relieves the user of liability for any violations occurring before or after receipt of the notice of violation. Nothing in this section shall limit the authority of the city to take any action, including emergency actions or any other enforcement action, without first issuing a notice of violation.

(B)	A violation of any provision of this chapter, wastewater discharge permit or order issued hereunder, or any other pretreatment standard or requirement is hereby declared a public nuisance and shall be corrected or abated as directed by the control authority. If any person discharges sewage, industrial wastes or other wastes into the city's treatment system contrary to this chapter, wastewater discharge permit or order issued hereunder, or any other pretreatment standard or requirement, the city attorney shall commence an action for appropriate legal or equitable relief or both in the Circuit Court of Marlboro County.

(Ord. 16-04-001, passed 4-19-16)

2016 S-3

Sewers	97

§ 56.64  COMPLIANCE; SCHEDULES AND ORDERS.

(A)	Compliance schedules. The control authority is hereby empowered to enter into compliance schedules, assurances of voluntary compliance or other similar documents establishing an agreement with the user responsible for the noncompliance. Schedules will include specific actions to be taken by the user to correct the noncompliance within a time period also specified by the schedules.

(B)	Consent orders. The control authority is hereby empowered to enter into consent orders, assurance of voluntary compliance, or other similar documents establishing an agreement with the User responsible for the noncompliance. The orders will include specific actions to be taken by the user to correct the noncompliance within a time period also specified by the order. Consent orders shall have the same force and effect as administrative orders issued pursuant to § 56.66.

(C)	Compliance order. When the control authority finds that an industrial user has violated or continues to violate any provision of this chapter or a wastewater discharge permit or order issued hereunder, or any other pretreatment standard or requirement, the control authority may issue an order to the user responsible for the discharge directing that the user come into compliance within a specified time. If user does not come into compliance within the time provided, sewer service shall be discontinued unless adequate treatment facilities, devices or other related appurtenances have been installed and are properly operated. Compliance orders may also contain other requirements as might be reasonably necessary and appropriate to address the noncompliance, including the installation of pretreatment technology, additional self-monitoring and management practices designed to minimize the amount of pollutants discharged to the sewer. A compliance order may not extend the deadline for compliance established for a pretreatment standard or requirement, nor does a compliance order relieve the user of liability for any violation, including any continuing violation. Issuance of a compliance order shall not be a bar against, or a prerequisite for, taking any other action against the user.

(Ord. 16-04-001, passed 4-19-16)

§ 56.65  SHOW CAUSE HEARINGS.

(A)	(1)	The control authority may order a user which causes or contributes to violations(s) of this chapter or discharge permit or order issued hereunder, or any other pretreatment standard or requirement, to show cause before the control authority why an enforcement action should not be taken.

(2)	A notice shall be served on the user, specifying the time and place of a hearing to be held, the proposed enforcement action and the reasons for the action, and a request that the user show cause why this proposed action should not be taken. The notice of the meeting shall be served by certified mail (return receipt requested) at least 15 days prior to the hearing. The notice may be served on any authorized representative of the user, as defined in § 56.01, and required by § 56.35(G). A show cause hearing shall not be a bar against, or prerequisite for, taking any other action against the user.

2016 S-3

98	Bennettsville - Public Works

(3)	Whether or not a duly notified industrial user appears as noticed, immediate enforcement action may be pursued.

(B)	At any public hearing, testimony taken before the hearing authority or any person designated by it must be under oath and recorded stenographically. The transcript so recorded will be made available to the hearing to any member of the public or any party to the hearing upon payment of the usual charges therefor. The hearing authority may itself conduct the hearing and take evidence, or may designate any of its members or any officer or employee to:

(1)	Issue in the name of the hearing authority notices of hearings requesting the attendance and testimony of witnesses and the production of evidence relevant to any matter involved in any hearings;

(2)	Take the evidence; and

(3)	Transmit a report of the evidence and hearing, including transcripts and other evidence, together with recommendations to the hearing authority for action thereon.

(Ord. 16-04-001, passed 4-19-16)

§ 56.66  CEASE AND DESIST ORDERS.

When the control authority finds that an industrial user has violated or continues to violate this chapter or any permit or order issued hereunder, or any other pretreatment standard or requirement, or that the user's past violations are likely to recur, the control authority may issue an order to the user to cease and desist all violation and direct those persons in noncompliance to:

(A)	Immediately comply with all requirements; and

(B)	Take appropriate remedial or preventive action as may be needed to properly address a continuing or threatened violation, including halting operations and terminating the discharge. Issuing a cease and desist order shall not be a bar against, or a prerequisite for, taking any other action against the user.

(Ord. 16-04-001, passed 4-19-16)

§ 56.67  EMERGENCY SUSPENSIONS.

(A)	The control authority may immediately suspend the wastewater treatment service and/or the industrial discharge permit of a user whenever the suspension is necessary in order to stop an actual or threatened discharge presenting or causing an imminent or substantial endangerment to the health or welfare of persons. The control authority may also immediately suspend a user's discharge, after notice and opportunity to respond, that threatens to interfere with the operation of the POTW, or which presents, or may present, an endangerment to the environment.

2016 S-3

Sewers	99

(B)	Any user notified of a suspension of the wastewater treatment service and/or the industrial discharge permit shall immediately stop or eliminate its contribution. In the event of a user's failure to immediately comply voluntarily with the suspension order, the control authority shall take steps as deemed necessary, including, but not limited to, immediate severance of the sewer connection or water service connection, to prevent or minimize the damage to the wastewater treatment system, the receiving stream or endangerment to any individuals. The control authority shall allow the user to recommence its discharge when the user has demonstrated to the satisfaction of the control authority, that the period of endangerment has passed, unless the termination proceedings set forth in § 56.66 are initiated against the user.

(C)	A user which is responsible, in whole or in part, for any discharge presenting irnminent endangerment shall submit a detailed written statement describing the causes of the harmful contribution and the measures taken to prevent any future occurrence to the control authority prior to the date of the hearing described in §§ 56.65 and 56.68.

(D)	Nothing in this section shall be interpreted as requiring a hearing prior to any emergency suspension under this section.

(Ord. 16-04-001, passed 4-19-16)

§ 56.68  TERMINATION OF DISCHARGE.

(A)	In addition to the provisions in § 56.36(F), any user who violates the following conditions is subject to discharge termination:

(1)	Violation of individual wastewater discharge permit or general permit conditions;

(2)	Failure to accurately report the wastewater constituents and characteristics of its discharge;

(3)	Failure to report significant changes in operations or wastewater volume, constituents, and characteristics prior to discharge;

(4)	Refusal of reasonable access to the user's premises for the purpose of inspection, monitoring, or sampling; or

(5)	Violation of the pretreatment standards in §§ 56.19 through 56.23.

(B)	Nothing in this section is exclusive and violators of this section may be subject to other penalties as prescribed by law and other enforcement sections of this chapter. Such user will be notified of the proposed termination of its discharge and be offered an opportunity to show cause under § 56.65 why the proposed action should not be taken. Exercise of this option by the control authority shall not be a bar to, or a prerequisite for, taking any other action against the user.

(Ord. 16-04-001, passed 4-19-16)

2016 S-3

100	Bennettsville - Public Works

§ 56.69  JUDICIAL REMEDIES; INJUNCTIVE RELIEF.

(A)	Whenever a person discharges sewage, industrial wastes or other wastes into the wastewater treatment system contrary to the provisions of this chapter, an order or permit issued hereunder, the control authority, through the city's attorneys may commence an action for appropriate legal and/or equitable relief in the Circuit Court for Marlboro County.

(B)	Whenever a user has violated or continues to violate the provisions of this chapter or permit or order issued hereunder, or any other pretreatment standard or requirement, the control authority, through counsel may petition the court for the issuance of a temporary or permanent injunction or both, as may be appropriate, which restrains or compels the activities on the part of the user. The control authority shall have remedies to collect these fees as it has to collect other sewer service charges. The control authority may also seek such other action as is appropriate for legal and/or equitable relief, including a requirement for the user to conduct environmental remediation. A petition for injunctive relief shall not be a bar against, or a prerequisite for, taking any other action against a user.

(Ord. 16-04-001, passed 4-19-16)

§ 56.70  PUBLICATION AND SEVERANCE.

(A)	Publication of users in significant noncompliance. The control authority shall publish annually, in a newspaper of general circulation that provides meaningful public notice within the jurisdictions served by the POTW, a list of the users which, at any time during the previous 12 months, were in significant noncompliance with applicable pretreatment standards and requirements. The term SIGNIFICANT NONCOMPLIANCE shall be applicable to all significant industrial users (or any other industrial user) that violates divisions (A)(3), (4) or (8) below and shall mean:

(1)	Chronic violations, defined here as those in which 66% or more of all the measurements taken for the same pollutant parameter taken during a six-month period exceed (by any magnitude) a numeric pretreatment standard or requirement, including instantaneous limits;

(2)	Technical review criteria (TRC) violations, defined here as those in which 33% or more of wastewater measurements taken for each pollutant parameter during a six-month period equals or exceeds the product of the numeric pretreatment standard or requirement including instantaneous limits, multiplied by the applicable criteria (1.4 for BOD, TSS, fats, oils and grease, and 1.2 for all other pollutants except pH);

(3)	Any other violation of a pretreatment standard or requirement (daily maximum, long-term average, instantaneous limit, or narrative standard) that the control authority determines has caused, alone or in combination with other discharges, interference or pass through, including endangering the health of POTW personnel or the general public;

2016 S-3

Sewers	101

(4)	Any discharge of a pollutant that has caused imminent endangerment to the public or to the environment, or has resulted in the control authority's exercise of its emergency authority to halt or prevent such a discharge;

(5)	Failure to meet, within 90 days of the scheduled date, a compliance schedule milestone contained in an individual wastewater discharge permit or a general permit or enforcement order for starting construction, completing construction, or attaining final compliance;

(6)	Failure to provide within 45 days after the due date, any required reports, including baseline monitoring reports, reports on compliance with categorical pretreatment standard deadlines, periodic self-monitoring reports, and reports on compliance with compliance schedules;

(7)	Failure to accurately report noncompliance; or

(8)	Any other violation(s), which may include a violation of best management practices, which the city determines will adversely affect the operation or implementation of the local pretreatment program.

(B)	Whenever a user has violated or continues to violate the provisions of this chapter or permit or order issued hereunder, or any other pretreatment standard or requirement, water service to the user may be severed and service will only recommence at the user's expense, after it has satisfactorily demonstrated its ability to comply.

(Ord. 16-04-001, passed 4-19-16)

§ 56.99  PENALTY.

(A)	Administrative fines. Notwithstanding any other sections of this chapter, any user who is found to have violated any provision of this chapter, or permits and orders issued hereunder, or any other pretreatment standard or requirement, shall be fined in an amount up to $2,000 per day per violation. Each day on which noncompliance shall occur or continue to occur shall be deemed a separate and distinct violation. In the case of monthly or other long-term average discharge limits, fines shall be assessed for each day during-the period of violation. Assessments shall be added to the user's next sewer service charge and the control authority shall have other collection remedies as he has to collect other service charges. Unpaid charges, fines and penalties shall constitute a lien against the individual user's property. Industrial users desiring to dispute the fine must file a request for the control authority to reconsider the fine within ten days of being notified of the fine. Where the control authority believes a request to have merit, he shall convene a hearing on the matter within 15 days of receiving the request from the user. Issuance of an administrative fine shall not be a bar against, or a prerequisite for, taking any other action against the user.

2016 S-3

102	Bennettsville - Public Works

(B)	Civil penalties.

(1)	Any user who has violated or continues to violate this chapter or any permit or order issued hereunder, shall, be liable to the control authority for a civil penalty of up to $2,000, plus actual damages incurred by the city per violation per day for as long as the violation continues. In addition, the control authority may recover reasonable attorney fees, court costs and other expenses associated with the enforcement activities, including sampling and monitoring expenses.

(2)	The control authority shall petition the court to impose, assess and recover the sums. In determining the amount of liability, the Court shall take into account all relevant circumstances, including, but not limited to the extent of harm caused by the violation, the magnitude and duration of the violation(s), any economic benefit gained by the user through failure to comply, corrective actions by the user, the compliance history of the user and any other factor as justice requires.

(C)	Criminal prosecution.

(1)	Violations, generally.

(a)	Any user who willfully or negligently violates any provision of this chapter or any orders or permits issued hereunder, or any other pretreatment standard or requirement shall, upon conviction, be guilty of a misdemeanor, punishable by a fine not to exceed $5,000 per violation per day or imprisonment for not more than one year or both.

(b)	A user who willfully or negligently introduces any substance into the POTW which causes personal injury or property damage shall, upon conviction, be subject to a penalty of up to $2,000 per violation, per day, or be subject to imprisonment, or both, as provided by state law. This penalty shall be in addition to any other cause of action for personal injury or property damage available under state law.

(c)	In the event of a second conviction, the user shall be punishable by a fine up to $2,000 per day per violation or imprisonment for not more than three years or both.

(2)	Falsification of information.

(a)	Any user who knowingly makes any false statements, representations or certifications in any application, record, report, plan or other document filed or required to be maintained by this chapter or discharge permit or order issued hereunder, or who falsifies, tampers with or knowingly renders inaccurate any monitoring device or method required under this chapter shall, upon conviction, be punished by a fine of not more than $5,000 per violation per day or imprisonment for not more than one year or both.

(b)	In the event of a second conviction, the user shall be punishable by a fine up to $2,000 per day per violation or imprisonment for not more than three years or both.

2016 S-3

Sewers	103

(D)	Additional penalty.

(1)	If a user whose violations(s) of this chapter is responsible for a violation of the city's NPDES permit and the assessment of a fine or penalty by SCDHEC on the city for the user caused violation, then the person whose violation is responsible for, the city's noncompliance shall be assessed a penalty of not less than that imposed upon the city by SCDHEC.

(2)	The city shall pursue a policy of recovering any and all economic benefit from noncompliance in the assessment of penalties under this chapter.

(3)	In addition to the penalties provided herein, the city may recover reasonable attorney fees, court costs, court reporter fees and other expenses of litigation by appropriate suit at law against the person found to have violated this chapter or the orders, rules, regulations and permits issued hereunder.

(4)	The city shall disconnect sewer service for any person who is more than 90 days in arrears with payment of monthly sewer service charges. Reconnection may be permitted after payment of all charge and penalties as herein provided.

(E)	Remedies nonexclusive. The remedies provided for in this chapter are not exclusive, the control authority may take any, all, or any combination of these actions against a noncompliant user. Enforcement of pretreatment violations will generally be in accordance with the city's enforcement response plan. However, the control authority may take other action against any user when the circumstances warrant. Further, the control authority is empowered to take more than one enforcement action against any noncompliant user.

(F)	Affirmative defenses.

(1)	Upset.

(a)	Any user which experiences an upset in operations that places in a temporary state of noncompliance, which is not the result of operational error, improperly designed treatment facilities, inadequate treatment facilities, lack of preventive maintenance or careless or improper operation, shall inform the control authority, or his defense, thereof, immediately upon becoming aware of the upset. Where the information is given orally, written report thereof shall be filed the user within five days of the oral notification. The report shall contain:

1.	A description of the upset, its cause and impact on the discharger's compliance status;

2.	The duration of noncompliance, including exact dates and times of noncompliance, and if the noncompliance is continuing, the day by which compliance is reasonably expected to be restored; and

2016 S-3

104	Bennettsville - Public Works

3.	All steps taken or planned to reduce, eliminate and prevent the recurrence of an upset.

(b)	A user which complies with the notification provisions of this chapter in a timely manner shall have an affirmative defense to any enforcement action except those penalties assessed under division (C) above, by the city for any noncompliance with this chapter, or a permit order issued hereunder by the user, which arises out of violations attributable to and alleged to have occurred during the period of the documented and verified upset.

(2)	Prohibited discharge standards. A user shall have an affirmative defense to an enforcement action brought against it for noncompliance with the general prohibitions in § 56.19(A) or the specific prohibitions in § 56.19(B) if it can prove that it did not know, or have reason to know, that its discharge, alone or in conjunction with discharges from other sources, would cause pass through or interference and that either:

(a)	A local limit exists for each pollutant discharged and the user was in compliance with each limit directly prior to, and during, the pass through or interference; or

(b)	No local limit exists, but the discharge did not change substantially in nature or constituents from the user's prior discharge when the city was regularly in compliance with its NPDES permit, and in the case of interference, was in compliance with applicable sludge use or disposal requirements.

(Ord. 16-04-001, passed 4-19–16)

2016 S-3